## Slide 1: D-NFV NFV Breaking Out of the Data Center
Presented by:
Yaakov (J) Stein
CTO

## Slide 2: Concretization and Virtualization
PHYSICS
LOGIC
dedicated hardware
ASIC
FPGA
special purpose processors
general
purpose
software
firmware
VIRTUALIZATION
CONCRETIZATION
Concretization means moving a task to the left
Justifications for concretization include :
  cost savings for mass produced products
  miniaturization/packaging constraints
  need for high processing rates
  energy savings / power limitation / low heat dissipation
Virtualization is the opposite - moving a task to the right
(although frequently reserved for the extreme case of HW → SW)

## Slide 3: Justifications for Virtualization
The justifications for virtualization are initially harder to grasp
  lower development efforts and cost
  flexibility and ability to upgrade functionality
  chaining multiple functions on a single platform
  facilitating function relocation
By function relocation we mean
moving the network function from its conventional place
to some other place (e.g., to a Data Center)
Relocation has received much attention in the networking community
since moving networking functions to Data Centers
often enables benefiting from economies of scale
This emphasis on this single reason for virtualization has been so strong
that it has led many to completely confuse virtualization and relocation
when in fact
nonvirtualized functions can be relocated (at the expense of CAPEX and truck rolls)
virtualized functions can remain in situ (will get to that in a moment)
Data Center

## Slide 4: Function placement
Telecomm functionalities tend to be placed in conventional locations
Customer Premises
Aggregation Point
Point of Presence
Core Network Edge
Data Center
Some telecomm functionalities really must reside at their locations
LoopBack testing (what would it mean to move LB to a data center?)
End-to-End security (why encrypt packets after they traverse the network )
Some should be left in the conventional locations
End-to-End performance monitoring (it wouldn’t be end-to-end – would it ?)
DDoS attack blocking (best to block as close to source as possible)
Some may be placed almost anywhere
Path Computation
Charging/billing functionality

## Slide 5: Distributed NFV
With Virtualized Network Functions (not virtualized network resources)
placement is no longer dictated by convention or equipment
placement can be optimally determined anywhere in the network
The idea of optimally placing virtualized network functions in the network
is called Distributed NFV
Placement decisions can be based on
resource availability (computational power, storage, bandwidth)
real-estate availability and costs
energy and cooling
management and maintenance
other economies of scale
function chaining order
policy
security and privacy
regulatory issues
…
Consider moving a DPI engine from where it is needed
and sending the packets to be inspected to a remote DPI engine
If bandwidth is unavailable or expensive or excessive delay is added
then DPI must not be relocated
even if computational resources are less expensive elsewhere!

## Slide 6: Some D-NFV criteria
Criterion | Description
Feasibility | Some functions can’t be relocated from customer site, e.g., loopback testing, end-to-end security, traffic conditioning, encryption, WAN optimization
Performance | Some functions perform better at the customer premises, e.g., end-to-end QoS, application QoE monitoring Some functions may degrade due to network constraints (bandwidth, delay, availability)
Cost | Needs for higher network performance and resiliency may lead to cost increases, even with Data Center economies of scale
Policy | Some functions need to be left near the customer due to corporate privacy, security, and access policies Regulatory restrictions (e.g., on moving data across jurisdictions) may also apply

## Slide 7: Relocation and CPEs
One relocation that has been actively discussed recently
is being called virtualization of the CPE (vCPE) (virtualization means relocation)
Here CPE functionality is virtualized and moved from the customer premises
leaving behind only minimal functionality (OAM, traffic conditioning)
Equally interesting is virtualization in the CPE
Here functionalities are moved to the customer premises
Customer Premises
Customer
Network
CPE
Network
Data Center
Customer Premises
Customer
Network
CPE
Network
Data Center
VNF
VNF
VNF
VNF

## Slide 8: Virtualization and relocation of CPE
pC
vC
pC
Partial Virtualization
vC
pvC
pvC
vC
vC
vC
vC
Full Virtualization
Full Relocation
Partial Relocation
p physical
v virtual
C CPE

## Slide 9: VM-enhanced NID
Virtualization in the CPE
requires a customer premises device capable of hosting VNFs
A reasonable device would be the Network Interface Demarcation device
For example, RAD has integrated an x86 module into its ETX2 L2/L3 NID
This device retains all its NID functionality (OAM, traffic conditioning)
and acquires the capability of hosting arbitrary software functions
The combined ETX/VM device is
located at the customer premises
under the control of the Service Provider
Thus the SP can rapidly download arbitrary functionalities to the NID
for its own purposes (diagnostics, visibility, blocking traffic, etc.)
as a Value Added Service for the customer (firewall, NAT, IDS, etc.)
without the need for installing any new network equipment

## Slide 10: Advantages of VM-enhanced NID
  The NID needs to be deployed in any case
  and the additional cost of the computational power is minimal
  On-site installation, maintenance, and energy costs
  are much lower than for multiple dedicated devices
  The marginal cost of a VNF is that of a software license plus OPEX
  VNFs can be downloaded on-demand and very rapidly
  and can be activated/deactivated/removed as required
  Multiple VNFs can be chained on a single device
  the only limitation being the module’s computational power and memory
  The CPU connects to the internal NID switch ports
  and so can operate on packets at various stages (ingress, in-process, egress)
  VAS VNFs can be offered on a trial basis
  enabling a “try and buy” approach

## Slide 11: ETX/VM architecture
The ETX/VM houses three virtual entities
  standard ETX NID (OAM, policing, shaping, etc.)
  VM infrastructure (hypervisor)
  VNFs that run on the VM infrastructure
The VNFs are managed by an NFV orchestrator
and are written by compliant vendors or by the Service Providers themselves
Network
ETX2
Customer Site
Customer
Network
Hypervisor
VNF
VNF
D-NFV
orchestrator

## Slide 12: Example: Packet Replication
Network
Hypervisor
Customer
Network
NNI
UNI
Classifier
Packet Replicator
D-NFV
Orchestrator
This simple VNF replicates particular packets, e.g., for
diagnostics
ad-hoc multicast
lawful interception
Management
System

## Slide 13: Example: Packet Editing
Network
Hypervisor
Customer
Network
NNI
UNI
Classifier
Packet Editor
D-NFV
Orchestrator
This simple VNF edits particular packet headers, e.g., to
swap/add/remove VLAN tags or MPLS labels
tunnel certain packets across another network
remark packet priorities
Management
System

## Slide 14: Example: NAT64
IPv6 Network
Hypervisor
NAT64
D-NFV
Orchestrator
This VNF stitches together IPv4 and IPv6 networks (RFC 6145)
traffic packets headers are rewritten
control protocols are interworked (ICMP, ARP, NDP, …)
Application Layer Gateways are implemented
IPv4 Network

## Slide 15: Example: Application Visibility
Network
Hypervisor
Customer
Network
NNI
UNI
DPI engine
Statistics
D-NFV
Orchestrator
This VNF is a probe for SP application type visibility
Application statistics are sent for display using specialized packets
The DPI engine is optimized for performance
Visibility
Display

## Slide 16: Example: Firewall
Network
Hypervisor
Customer
Network
Firewall VLANs
Pass-through VLANs
NNI
UNI
Firewall VLANs
Firewall Management
Open vSwitch
Firewall VNF
D-NFV
Orchestrator
As a final example, consider a firewall VAS (demo at the RAD booth)
The hypervisor and vSwitch are Open Source software
The firewall VNF is a third-party application
rule rule
rule rule
rule rule

## Slide 17: D-NFV Placement Problems
Pure D-NFV placement optimization problem
Given:
the path taken by the traffic (and the availability of extra bandwidth if needed)
the VNF(s) to be installed, including computational requirements
for multiple VNFs – the (partial) ordering of VNFs
places where computational resources are available, and present loadings
D-NFV criteria and constraints
Find the optimal D-NFV placement(s)
Joint PC/D-NFV optimization
Given:
traffic source and sink points
service bandwidth and delay requirements
the VNF(s) to be installed, including computational requirements
for multiple VNFs – the (partial) ordering of VNFs
places where computational resources are available, and present loadings
D-NFV criteria and constraints
Find the optimal path and VNF placement(s)

## Slide 18: Summary
One should differentiate between Virtualization and Relocation
NFV means Network Function Virtualization
not necessarily relocation to Data Centers
Distributed NFV means placing VNFs in their optimal location
which is frequently at the customer premises
There are many advantages to a VM-enhanced customer NID
and many useful VNFs for it
D-NFV placement is a non-trivial orchestration problem