## Slide 1: Part 4 Signal Processing Applications
0368.3464
עיבוד ספרתי של אותות
Digital Signal Processing for Computer Science
AKA
Digital Signal Processing – Algorithms and Applications

## Slide 2
Signal similarity

## Slide 3: Signal similarity
We often need to know how similar two signals x and y are
for example, to detect the appearance of a single in noise
In radar we transmit a known signal
the signal propagates in space until it is reflected by a target
it then travels back and is received by the radar receiver
By accurately detecting the exact time that the signal is received
and subtracting the exact time it was transmitted
we can deduce the distance to the target
However, due to
the 1/r2 propagation loss
the minute amount of energy reflected
the signal received is very weak
while the noise may be large
We need a very sensitive way to detect the known signal in noise

## Slide 4: Signal similarity
To compare two signals
we can compute the difference signal δ = x – y
and define similarity as its energy Eδ being small
But that doesn’t work if (with respect to x)
y has some gain
y is shifted in time
For example, if y = g x then the difference is δ = (1-g) x
which is only small if g≈1
We can derive something better from the energy Eδ
Eδ = - )2
= 2 – 2 + 2
= Ex – 2 Cxy + Ey
Cxy is called the (cross)correlation between x and y

## Slide 5: Correlation
Eδ = Ex – 2 Cxy + Ey
where Ex and Ey are the (constant) energies of the 2 signals
Note that when Eδ is minimal, Cxy is maximal
so we say the signals are correlated when Cxy is large
Cxy is still large even if y has arbitrary gain with respect to x
since the gain is captured in the energy component
For example, if y = g x (and thus Ey = g2 Ex)
then Cxy = = g = g Ex
What do we mean by large?
If y = g x then Cxy =
so a simple way to gauge the size of cross-correlation
is to compare it with (it won’t be equal because of noise!)
However, Cxy will not indicate similarity if y is shifted in time

## Slide 6: Correlation
If Cxy is positive and large
then x and y are correlated (similar)
If Cxy is negative and large
then x and y are anticorrelated
If Cxy is zero (or very small)
then x and y are uncorrelated (different)

## Slide 7: Correlation with lags
To take care of time shifts with define (m is called the correlation lag)
Cxy(m) =
(m is called the correlation lag)
We now look for its maximum value (its peak)
This peak corresponds to the optimal time shift
if there the correlation is significant (using the same criterion as before)
then we have found our similar signal
Note the difference between correlation and convolution
in correlation both indexes increase
in convolution one increases one decreases

## Slide 8: Highly correlated signals
gain
gain and noise
gain and lag

## Slide 9: Financial indicators
DAX, Dow Jones, Nasdaq and gold prices from 2011-2016
Which signals are correlated? Anticorrelated?
Can you use this for prediction?

## Slide 10: Autocorrelation
We can define the autocorrelation Cxx(m) =
which tells us how similar the signal is to itself
Of course a signal is always similar to itself!
But we use autocorrelation to see how similar a signal is
to a time shifted version of itself
A periodic signal has peaks at lags that are multiples of its period!
Since |cxx(m)| ≤ Ex it is useful to define the normalized autocorrelation
cxx(m) = Cxx(m) / Ex
where |cxx| ≤ 1
Why can autocorrelation be more accurate than using the FFT?

## Slide 11: Wiener filter
Pulse radars transmit a short (and thus low energy) distinctive pulse
and receive a delayed, weak, noisy copy after time t = 2 * c * R
The Wiener filter finds t by building an MA filter
with coefficients equal to the time reversed signal
The MA’s convolution actually performs a correlation
t

## Slide 12: Prediction
Wiener’s famous paper was named
Interpolation, extrapolation and smoothing of stationary time series
Where in modern terminology:
smoothing = low-pass filtering
interpolation = resampling (sampling at different time instants)
extrapolation = prediction
We previously saw how Yule predicted sun-spots via an AR process
* = where s* is the estimate of s
Let’s directly derive the coefficient b for the simplest case (M=1)
We want to minimize the energy of the error signal e = y*-y
2 = = (1+2)Es – 2Cs(1)
Differentiating and setting equal to zero we find = Cs(1) / Es = cs(1)
So, there is a connection between prediction and autocorrelation!
More generally, the coefficients are given by Yule Walker equations!

## Slide 13: Adaptive filters
We often would like to remove noise from a noisy signal
Sometimes we can access a signal that is highly correlated to the noise
For example, assume 2 microphones
1. air conditioner noise qn
2. speech xn + filtered air conditioner noise q’
In the simplest case
the filtering is a single-tap MA filter which adds a qn-m
so yn = xn + a qn-m where a and m are unknown
The idea is to find a and m by adapting our estimates of them
so this is called an adaptive filter
If a and q change over time
or even when we simply alter our estimates of them
then this is not a filter since it is not time invariant
q
x
y = x+q’

## Slide 14: Adaptation
We can assume that
the desired signal x and
the noise
are uncorrelated
By finding the maximum cross-correlation
between q and y=x+q’ (which only looks for q!)
we can determine m and thus qn-m
But how do we find a ?
Estimate x*n = yn - c qn-m = xn + (a-c) qn-m
x
q
-
a
x*
c

## Slide 15: The energy parabola
x*n = xn + (a-c) qn-m
So Ex* = < x*2 > = < x2 > + (a-c)2 < q2 > + 2 (a-c) <x q>
Since x and q are uncorrelated the last term is zero
The energy is parabolic in c with a single minimum
Ex*
c
a

## Slide 16: Adaptation
Starting from x*n = xn + (a-c) qn-m
The global minimum is for c=a and there x*n = xn
To find c we need to minimize the energy of x*n as a function of c
This minimization is typically done via gradient descent (AKA steepest descent)
What if we receive the noise and echoes of it? yn = xn + Σm am qn-m
The same thing can be done for a M-tap filter
using M-dimensional gradient descent
Ex*
c
a

## Slide 17: Gradient descent
E
c
In gradient descent we choose a step size λ
at each step we estimate the gradient (derivative of E) d
and correct c at each step by c ← c - λ d
The gradient points in the direction that E increases
so we move in the opposite direction (minus sign)
The larger the gradient the further we move
for more complex problems
the energy is not parabolic
and may contain local minima
choosing the step size
can be important!

## Slide 18: Echo cancellation
Another common use of adaptive filters is echo cancellation
Acoustic Echo Cancellation
e.g., for car hands-free units
Line Echo Cancellation
hybrid
hybrid

## Slide 19: Echo suppressors
Telephony hybrids are not perfect
leaking some amount of echo is sent back to the speaker
If the echo delay is < 20 ms then this is not noticed
but round-trip delay for US coast-to-coast is > 50 ms
and for satellite conversations the delay is > ½ second
Before the advent of DSPs echo was removed by echo suppressors
that chose the louder direction and blocked the opposite direction
effectively making telephone conversations half-duplex
(this still sometimes happens with simple office phones)
For non-speech (fax, modems) echo suppressors are turned off
by sending a 2100 Hz tone
Echo suppression is a waste of full-duplex infrastructure
conversation is unnatural
hard to break in
speaker hears dead line (so telephones artificially add sidetone)
LEC was one of the first applications of DSPs

## Slide 20: Echo cancellers
In a simplistic model of LEC the near end simply estimates the echo
and subtracts it to send clean (echo-less) speech to the far end
(of course the far end does the same)
Real LECs have additional elements, including
double-talk detectors (Geigel algorithm)
to freeze adaptation when both sides are speaking
nonlinear processing (center clipping) to remove residual echo
near end
far end
-
clean speech
echo path
speech
+
echo

## Slide 21: Realistic LEC

## Slide 22: LEC in action
The LEC mechanism
places samples received from the far-end into the X buffer
convolves them with the current filter (called the H register)
obtaining the echo estimate
subtracts the echo estimate from the near-end samples
How is the filter adaptation done?
Assume that only the far-end subscriber is talking
then the signal at the input to the subtracter is unwanted echo generated by the near-end hybrid and telephone
The adaptation mechanism varies the filter coefficients
minimizing the energy at the output of the subtracter
If the far-end is quiet or double-talk is detected
the adaptation algorithm automatically stops updating

## Slide 23: Equalization
A problem that arises in data communications
We can model the channel distortion as
filtering i.e.,
adding noise
Recovering the original signal
requires applying the inverse of the channel filter (equalization)
i.e.,
For this we need to
find the channel filter coefficients
invert the filter
Equalizers are also used in stereo audio systems. Why ?
transmitter
receiver
distorting
channel

## Slide 24: Multipath
What happens when a signal is received over a primary (shortest) path
and also over delayed paths (e.g. reflections off buildings) ?
The composite signal contains echoes
and is thus an MA filtered version of the original
primary path
delayed paths
+
min
delay
max delay

## Slide 25: Finding the equalizer
If we start the transmission with a known signal
then finding the channel filter is a system identification problem
In particular, if we assume that the channel filter
is MA then we need to solve Wiener-Hopf equations
and the inverse filter will be AR why?
is AR then we need to solve Yule-Walker equations
and the inverse filter will be MA why?
Sometimes we can’t transmit a special known sequence - why?
for example, receiver may turn on at any time
then we need blind equalization
And even if we can, what if the channel changes over time? why?
for example, a mobile receiver
Then we need to adapt the equalizer over time
if we can derive a measure of received SNR
we can use gradient descent

## Slide 26: Using the equalizer
There are two ways to apply equalization G to compensate for H
at the receiver x = G y = G H x = H-1 H x
at the transmitter (Tomlinson precoding) : transmit x’ = G x
and receiver automatically sees y = H G x = H H-1 x
If the channel filter is not AR then the second way is better – why?
Because at frequencies where the filter has zeros
the channel frequency response is not invertible
That is, if at ω0 we have H(ω0)=0
then no G(ω0) can obey G(ω0) H(ω0) = 1
and so information there is lost
Even if H(ω0) is not exactly zero, but very small H(ω0) ≈ 0
G(ω0) will have to be very large
and will lead to noise amplification
(we have been neglecting the additive noise until now ...)
However, Tomlinson requires a back-channel!

## Slide 27
Speech signal processing

## Slide 28: Application: Speech
Speech is a wave traveling through space
at any given point in space it is a signal in time
The speech values are pressure differences (or molecule velocities)
There are many reasons to process speech, for example
speech storage / communications
speech compression (coding)
speed changing, lip sync
text to speech (speech synthesis)
speech to text (speech recognition)
translating telephone
speech control (commands)
speaker recognition (forensic, access control, spotting, …)
language recognition, speech polygraph, …
voice fonts

## Slide 29: Speech in the time domain
D IGI T A L S I GNA L PROCESSING
Why don’t we see the letters?

## Slide 30: Speech in the frequency domain
Why don’t we see the letters?

## Slide 31: Phonemes
A phoneme is defined to be the smallest acoustic unit
that can change meaning
Different languages have different phoneme sets
and their speakers hear sounds differently
in Hebrew there is no TH phoneme, so speakers substitute Z
in Arabic there is no P phoneme, so speakers substitute B
in English there is no כ phoneme, so speakers substitute K
in Japanese there is a single phoneme
somewhere between English R and L
Some languages have many phonemes
Danish has 25 different vowels
Taa has over 150 consonants
Xhosa has 3 different click sounds
Some have very few
Piraha has 3 vowels and 8 consonants
Hawaiian has only 3 consonants

## Slide 32: Some phoneme types
Vowels front (heed, hid, head, hat) mid (hot, heard, hut, thought) back (boot, book, boat) dipthongs (buy, boy, down, date) Semivowels liquids (w, l) glides (r, y) | Consonants nasals (murmurs) (n, m, ng) stops (plosives) voiced (b,d,g) unvoiced (p, t, k) fricatives voiced (v, that, z, zh) unvoiced (f, think, s, sh) affricatives (j, ch) whispers (h, what) gutturals ( ח ,ע ) clicks etc. etc. etc.

## Slide 33: Speech sampling
Telephony speech is from 200 to 4000 Hz
this is not enough for all sounds we can hear
not really even enough for speech (e.g., S - F)
high quality audio is from 20 Hz to over 20 kHz
By the sampling theorem we need 8000 samples per second
high quality audio typically sampled at 44.1 / 44 / 48 kHz
If we sample at 8 bits per sample
we perceive significant quantization noise (see next slide)
So, let’s assume we should sample at 16 bits per sample
actually 13-14 bits is enough
So we need 8000 samples/sec * 16 bits/sample = 128 kbits/sec
to faithfully capture telephony quality speech
Information theory tells us that speech actually only carries
a few bits per second
So we should be able to improve this
but we need to learn more about the speech signal!

## Slide 34: What’s quantization noise?
When we quantize a signal value sn to the closest integer (or rational)
we add an error value xn = sn + qn
Assuming the qn samples are uncorrelated
the quantization noise is white noise
We hear white noise as a hiss
qn ε [-½ 2-n, ½ 2-n]
(or [-½ 2-n, ½ 2-n] if we assume the signal is in [-1 , 1])
So the more bits we use the better the Signal to Noise Ratio
Each additional bit reduces the SNR by a factor of 2 (3 dB)

## Slide 35: Speech biology
To understand the speech signal
we need to learn some biological signal processing
There are two separate systems of interest
speech generation system
  lungs
  windpipe
  vocal folds (cords)
  vocal tract (mouth cavity, tongue, teeth, lips, uvula)
  Broca’s area (in left hemisphere)
speech recognition system
  outer ear
  ear drum and hammer
  cochlea, organ of Corti (cilia)
  auditory nerve
  medial geniculate nucleus (in thalamus)
  auditory cortex and Wernicke’s area (in superior temporal gyrus)
These two systems are not well matched

## Slide 36: Speech Production Organs
Esophagus
Nasal
cavity
Mouth
cavity
Tongue
Larynx
Trachea
Uvula
Brain
Lungs
Pharynx
Teeth
Lips
Hard Palate
Velum

## Slide 37: Speech Production
Air from lungs is exhaled into trachea (windpipe)
Vocal cords (folds) in larynx can produce periodic pulses of air
by opening and closing (glottis)
Throat (pharynx), mouth, tongue and nasal cavity modify air flow
Teeth and lips can introduce turbulence
Basic function – filter an excitation signal
(we will see that the filter can be modeled as an AR filter)

## Slide 38: Hearing Organs

## Slide 39: Hearing Organs
Sound is air pressure changing over time (and propagating through space)
Sound enters the external ears which
collect as much sound energy as possible (like a satellite dish)
differentiate between right/left and front/back
even differentiate between up and down
Sound waves impinge on outer ear enter auditory canal
Amplified waves cause eardrum to vibrate
Eardrum separates outer ear from middle ear
The Eustachian tube equalizes air pressure of middle ear
Ossicles (hammer, anvil, stirrup) amplify vibrations
Oval window separates middle ear from inner ear
Stirrup excites oval window which excites liquid in the cochlea
The cochlea is curled up like a snail
The basilar membrane runs along middle of cochlea
The organ of Corti transduces vibrations to electric pulses
Pulses are carried by the auditory nerve to the brain

## Slide 40: Cochlea
Cochlea has 2 1/2 to 3 turns (for miniaturization)
were it straightened out it would be 3 cm in length
The basilar membrane runs down the center of the cochlea
as does the organ of Corti
15,000 cilia (hairs) contact the vibrating basilar membrane
and when it vibrates they release neurotransmitters
stimulating 30,000 auditory neurons
Cochlea is wide (1/2 cm) near oval window and tapers towards apex
and is stiff near oval window and flexible near apex
hence high frequencies cause vibrations near the oval window
while low frequencies cause section near apex to vibrate
Basic function – Fourier Transform
(by overlapping bank of bandpass filters)

## Slide 41: Voiced vs. Unvoiced Speech
We saw that air from the lungs passes through the vocal cords
When open the air passes through unimpeded
When laryngeal muscles close them glottal flow is in bursts
When glottal flow is periodic we have voiced speech
basic interval/frequency called the pitch (f0)
pitch frequency is between 50 and 400 Hz
You can feel the vocal cord vibration
by placing your fingers on your larynx
A laryngeal microphone directly perceives the sound at this point
even opening you mouth very wide doesn’t work very well
Vowels are always voiced (unless whispered)
Consonants come in voiced/unvoiced pairs

## Slide 42: Exercise
Which are voiced and which are unvoiced ?
B, D, F, G, J, K, P, S, T, V, W, Z,
Ch, Sh, Th (the), Th (theater), Wh, Zh
Which unvoiced phoneme matches the voiced one?
B
D
G
V
J
Th (the)
W
Z
Zh

## Slide 43: Excitation spectra
Voiced speech is periodic and so has line spectrum
Pulse train is not sinusoidal due to short pulses of air
and is rich in harmonics (amplitude decreases about 12 dB per octave)
Unvoiced speech is not periodic
Common assumption : white noise (turbulent air)
f
f
pitch

## Slide 44: Effect of vocal tract
So what is the difference between all the (un)voiced sounds?
The sound exiting the larynx enters the mouth cavity and is filtered
Mouth and nasal cavities have resonances (poles)
similar to blowing air over a bottle
Thus the sound exiting the mouth is periodic (due to periodic excitation)
but with some harmonics strong and some weak
Resonant frequencies depend on geometry
in particular mouth opening, tongue position, lip position

## Slide 45: Effect of vocal tract - cont.
Sound energy at resonant frequencies is amplified
Frequencies of peak amplification are called formants
F1
F2
F3
F4
frequency response
frequency
voiced speech
unvoiced speech
F0

## Slide 46: Cylinder model(s)
Rough model of throat and mouth cavity (without naval pathway)
With nasal pathway
destructive
interference
Voice
Excitation
Voice
Excitation

## Slide 47: Formant frequencies
Peterson - Barney data (note the “vowel triangle”)
f1
f2
AE = hat
AH = hut
AO = ought
EH = head
ER = hurt
IH = hit
IY = heat
UH = hood
UW = who

## Slide 48: Sonograms
Which sounds are voiced?
Where is the pitch?
Where are the formants?

## Slide 49: Simple model for speech generation
synthesis
filter
White Noise
Generator
Pulse
Generator
U/V
switch
G
s

## Slide 50: LPC Model
This model was invented by Bishnu Atal (Bell Labs) in 1960s
pulse generator produces a harmonic rich periodic impulse train
white noise generator produces a random signal
U/V switch chooses between voiced and unvoiced excitation
varying gain allows to speak loudly or softly
(typically placed before the filter)
LPC filter amplifies formant frequencies
(no zeros but peaks - all-pole or AR IIR filter)
Note: standard LPC doesn’t work well for nasals
destructive interference creates zeros in the frequency response
output resembles true speech to within modeling error

## Slide 51: Can LPC compress speech?
Let’s estimate the number of bits/second required to
capture speech (for transmission or storage) using the LPC model
we need to model several times per phoneme
  no-one can produce more than a few phonemes per second
  20-100 frames per second is reasonable, let’s assume 25
we need to specify the pitch (between 50 and 400) in Hz
  1 byte is more than enough (no-one hears the difference of 1 Hz!)
we need 1 bit for the U/V switch
  but don’t have to waste a bit
  since we can encode as pitch with zero frequency
we need to capture the gain
  1 byte is enough (our ear is not that sensitive to small gain changes)
the AR filter has 4 formants
  so we need 8 values (4 frequencies and 4 amplitudes or 8 poles)
  and once again will assume 1 byte for each
Altogether we need 25 * (10 bytes * 8 bits/byte) = 2000 bits/sec
much better than 128,000 bits/sec

## Slide 52: LPC ?
Why is this model called Linear Predictive Coding ?
The synthesis filter performs
n = Sm bm sn-m
which predicts the next signal sample
based on a linear combination of previous samples
Most of the time we can forget about the glottal excitation
but this introduces an error en
So we define
n = en + Sm bm sn-m
This defines a classic AR model, solvable using Yule-Walker

## Slide 53: How do we do it?
Given a frame of speech samples (x0, x1, x2, ... xN-1)
how do we find the LPC parameters?
the gain is easy to find – it requires calculating the energy
U/V can be found by observing the spectrum
if lines then voiced, if continuous then unvoiced
the pitch can be determined by
  lowest spectral peak or frequency difference between peaks
  autocorrelation
since the input to the AR filter can now be created
and the output is the speech samples
we now have an AR filter system identification problem
so the filter can be found by solving the Yule-Walker equations

## Slide 54: Does it work?
An early commercial use of LPC
was the Texas Instruments Speak & Spell chip
which used LPC-10 (10 AR coefficients)
An early software implementation was Klattalk
Pure LPC speech sounds robotic (Steven Hawking speech) because
we need to add prosodic modeling
we need to post process to clean up estimation errors
e.g., pitch doubling
we need to add frame-to-frame processing
e.g., pitch needs to change smoothly
but most importantly
pitch pulses are not deltas or on-off rectangles
they have waveforms that influence the sound

## Slide 55: Better speech compression
Compressing telephony quality speech
was once a tremendously important problem
The International Telecommunications Union set goals
to reduce speech transmission rates by factors of 2
We can thus compare:
128 kbit/sec – linearly quantized speech
64 kbit/sec – Pulse Code Modulation (logarithmic quantization)
32 kbit/sec – Adaptive Delta PCM
16 kbit/sec was never standardized
8 kbit/sec – Code Excited LPC
But we now need to understand some psychophysics

## Slide 56: Psychophysics
Psychophysics is the subject that combines psychology and physics
Its fundamental question is the connection between
external physical values (light, sound, etc.)
internal psychological perception
Ernst Weber was one of the first to investigate of the senses
In a typical experiment
a subject is asked in which hand there are more coins
1 coin in 1 hand and 2 coins in the other is easily noticeable
10 coins in 1 hand and 11 coins in the other is just noticeable
41 coins in 1 hand and 42 in the other is not noticeable
But how could this be?
Can one notice the difference of 1 coin or not?

## Slide 57: Weber
Weber defined the concept of the Just Noticeable Difference (JND) the minimal change produces a noticeable difference
Weber’s important discovery was that JND varied with signal strength
In fact, Weber found
the sensitivity of a subject to X is in direct proportion to the X itself
that is
one notices adding a specific percentage not an absolute value
D I = k I
Thus
the number of noticeable additional coins
is proportional to the number of coins
and the same is true for
saltiness of salty water
length of lines
strength of sound

## Slide 58: Fechner’s law
Gustav Theodor Fechner was a student of Weber
While viewing the sun in order to discover JNDs he was blinded
He later regained his sight and took this as a sign
that he would solve the psychophysical problem
Simplest assumption: JND is single internal unit
Weber’s law says we perceive external values multiplicatively
Fechner concluded that internal unit is the log of the external one:
Y = A log I + B
People celebrate the day he discovered this
as Fechner Day (October 22 1850)

## Slide 59: Dynamic range
Logarithms are compressive
Fechner’s law explains the fantastic ranges of our senses
Sight (retinal excitation)
minimum: single photon
maximum (harm threshold): direct sunlight
ratio: 1015
Hearing (eardrum movement)
minimum: < 1 Angstrom 10-10 meters
maximum (harm threshold): >1 mm (behind a jet plane)
ratio: 108
Alexander Graham Bel defined to be log10 of power ratio
A decibel (dB) one tenth of a Bel
d(dB) = 10 log10 P1 / P2

## Slide 60: Fechner’s law for sound amplitudes
According to Fechner’s law, we are more sensitive at lower amplitudes
We perceive small differences when the sound is weak
but only perceive large differences for strong sounds
Companding is the compensation
for the logarithmic nature of speech perception
We need to adapt the logarithm function
to handle positive/negative signal values
If we could sample non-evenly
then this can be exploited for speech compression

## Slide 61: Fechner’s law for sound frequencies
octaves, well tempered scale
Critical bands
Frequency warping
Melody 1 KHz = 1000, JND afterwards M ~ 1000 log2 ( 1 + fKHz )
Barkhausen can be simultaneously heard B ~ 25 + 75 ( 1 + 1.4 f2KHz )0.69
excite different basilar membrane regions
f
12 2

## Slide 62: 2 more psychological laws
Respond to changes
Our senses respond to changes – not to constant values
Masking
Strong tones block weaker ones at nearby frequencies
f

## Slide 63: PCM
8 bit linear sampling (256 levels) is noticeably noisy
But due to
  prevalence of low amplitudes in generated speech
  logarithmic response of ear
we can use 8-bit logarithmic sampling ( with sgn(s) * log(|s|) )
G.711 gives 2 different logarithmic approximations
m-law
A-law
Although very different looking they are nearly identical
G.711 standard further approximates these expressions
by 16 staircase straight-line segments (8 negative and 8 positive)
Note that m-law has horizontal segment through the origin (plus and minus zero)
while A-law has a vertical segment
North America m = 255
Rest Of World
A = 87.56

## Slide 64: Logarithmic sampling

## Slide 65: DPCM
Due to low-pass character of speech excitation
differences are usually much smaller than signal values
and hence require fewer bits to quantize
This would not be the case for white noise!
Simplest Delta-PCM (DPCM) : quantize first difference signal Ds
Delta-PCM : it is even better to quantize
the difference between the signal and its prediction
n = p ( sn-1 , sn-2 , … , sn-N ) =
Since we predict using linear combination
this is a simple type of linear prediction
Delta-modulation (DM) : use only the sign of difference (1bit DPCM)
Sigma-delta (1bit) sampling : oversample, DM, trade-off rate for bits

## Slide 66: Deltas are usually small
The first difference requires fewer bits
if 4 bits is enough then we need 32 kb/s

## Slide 67: DPCM with prediction
If the linear prediction works well, then the prediction error
en = sn - n
will be lower in energy and whiter than sn itself !
Only the error is needed for reconstruction,
  since the predictable portion can be predicted sn = n + en!
sn
prediction
filter
sn
en
-
prediction
filter
n
n

## Slide 68: Open loop prediction
The encoder (linear predictor) is present in the decoder
  but there runs as feedback
The decoder’s predictions are accurate with the precise error en
but it gets the quantized error n
and as the error accumulates the signals diverge!
sn
-
Q
PF
n
PF
IQ
n

## Slide 69: Side information
There are two ways to solve the error accumulation problem ...
The first way is to send the prediction coefficients
  from the encoder to the decoder
  and not to let the decoder derive them
The coefficients thus sent are called side-information
Using side-information means higher bit-rate
(since both n and the coefficients must be sent)
The second way does not require increasing bit rate

## Slide 70: Closed loop prediction
To ensure that the encoder and decoder stay “in-sync”
  we put the entire decoder
  including quantization and inverse quantization
  into the encoder
Thus the encoder’s predictions are identical to the decoder’s
  and no model difference accumulates
sn
sn
IQ
PF
-
Q
en
PF
IQ
en

## Slide 71: Two more forms of error
For DM there is another source of error (that depends on step size)
D OK
D too small
D too large
D much too large

## Slide 72: Adaptive DPCM
Speech signals are very nonstationary
We need to adapt the step size to match signal behavior
  increase D when signal changes rapidly
  decrease D when signal is relatively constant
Simplest method (for DM only):
  if present bit is the same as previous multiply D by K (K=1.5)
  if present bit is different, divide D by K
  constrain D to a predefined range
More general method :
  collect N samples in buffer (N = 128 … 512)
  compute standard deviation in buffer
  set D to a fraction of standard deviation
    send D to decoder as side-information or
    use backward adaptation (closed-loop D computation)

## Slide 73: G.726
G.726 (standard for international telephony) has
  adaptive predictor
  adaptive quantizer and inverse quantizer
  adaptation speed control
  tone and transition detector
  mechanism to prevent loss from tandeming
computational complexity relatively high (10 MIPS)
32 kbps toll quality
24 and 16 Kbps modes defined, but not toll quality
G.727 same rates but embedded for packet networks
ADPCM only exploited general low-pass characteristic of speech
What is the next step?

## Slide 74: AVQSBC
A good quality 16 kb/s speech encoder is obtained
by exploiting Fechner’s law for sound frequencies
The idea is to use Sub-Band Coding
We divide the signal in the frequency domain
using perfect-reconstruction band-pass filters
The frequency widths are small at low frequencies
but large at high frequencies
Each subband is separate quantized using Vector Quantization
This technique was never standardized for speech
but SBC was standardized for music as MP3 audio
0 Hz
4000 Hz

## Slide 75: LPC10
For military-quality voice
180 sample frame (44.4 frames per second)
are encoded into 54 bits as follows:
Pitch + U/V (found using AMDF) 7 bits
Gain 5 bits
10 reflection coefficients
  first two coefficients converted to log area ratios
  L1, L2, a3, a4 5 bits each
  a5, a6, a7, a8 4 bits each
  a9 3 bits a10 2 bits 41 bits
1 sync bit 1 bit
54 bits 44.44 times per second results in 2400 bps
By using VQ one could reduce bit rate to under 1 Kbps!
LPC-10 speech is intelligible, but synthetic sounding
  and much of the speaker identity is lost !

## Slide 76: CELP
The true sn is obtained by adding back the residual error signal
sn = n + en
So if we send en as side-information we can recover sn
en is smaller than sn so may require fewer bits !
but en is whiter than sn so may require many bits!
Can we compress the residual?
Note that the residual error is actually the LPC filter’s excitation
The idea behind Code Excited Linear Prediction
is to encode possible excitations in a codebook of waveforms
and to send the index of the best codeword

## Slide 77: Analysis By Synthesis
To find the best code word we try them all (exhaustive enumeration)
although algebraic tricks save computation
We choose the code word with the least error
sn
CB
.
.
.
LPC
-
find
minimum
Compute
energy

## Slide 78: Perceptual weighting
But we don’t want the approximation
that looks the most like the real signal
We want the approximation
that sounds the most like the real signal
Now is the time to use psychophysics
Instead of computing the energy of the difference
we use a perceptual measure of similarity
that takes masking, etc. into account

## Slide 79: G.729
The standard speech compression in cellular
and very popular in Internet and other applications
Encodes 10 ms frames (100 frames per second) into 80 bits
resulting in 8000 bits per second
filter coefficients 18 bits pitch 8 bits
gain CB 14 bits adaptive CB 5 bits
pulse positions 26 bits pulse signs 8 bits parity check 1 bit

## Slide 80: Speech recognition
You might think that speech recognition could be performed thus:
extract speech features (e.g., LPC, Cepstrum) for speech frames
classify several successive frames into phonemes
combine phonemes into words
Unfortunately, that doesn’t work for many reasons
phonemes are pronounced differently depending on context
phonemes are pronounced differently depending on accent
phonemes may not be pronounced at all in rapid speech
nonlinear time warping

## Slide 81: Backtracking
The lower levels of the human auditory tentatively identify
the most probable phoneme
But as we continue listening
the higher levels continuously backtrack
and select lower probability ones if needed
To understand this backtracking we can use an analogy
from even higher levels of speech understanding
What does the word FIRE mean in the following sentence?
THE MAN SHOUTED
FIRE !
FIRE THE GUN !
FIRE THE GUN MAKER !

## Slide 82: Why don’t we notice this?
All of this happens unconsciously in the background
but involves higher levels of the cortex
Example 1
People who do not understand a language
can not reliably transcript phonemes in that language
Example 2
People who understand a language well
can successfully understand in very low SNR
Example 3
What am I saying?
HOW TO RECOGNIZE SPEECH
HOW TO WRECK A NICE BEACH

## Slide 83: Levenshtein distance
Automatic typing correction mechanisms and spelling correction
find the closest known word to an unknown one
How do we define closeness?
The Levenshtein distance between 2 strings (not necessarily equal length)
is defined as the minimal cost to transform 1 string to the other
Where each of the following has a defined cost
deletion digital → digtal
insertion signal → signall
substitution processing → prosessing
  in typing the cost may depend on how close the keys are
  in spelling correction the cost may depend on the sounds
What is the unity weighted Levenshtein distance
between digital and dijtal?
How do we find the minimum cost?

## Slide 84: Levenshtein distance (unity weighting)
What is the Levenshtein distance between prossesing and processing ?
p r o c e s s i n g
p r o s s e s i n g
Rules:
1 enter square
from left (deletion) cost = 1
2 enter square
from under (insertion) cost = 1
3a enter square
from diagonal
and same letter cost = 0
3b enter square
from diagonal
and different letter
(substitution) cost = 1
4 Always use minimal cost

## Slide 85: Levenshtein distance - cont.
Start with 0 in the bottom left corner
9
8
7
6
5
4
3
2
1
0 1 2 3 4 5 6 7 8 9
p r o c e s s i n g
p r o s s e s i n g
0

## Slide 86: Levenshtein distance - cont.
Continue filling in table
9
8
7
6
5
4 3 2 2 2
3 2 1 1 2
2 1 0 1 2
1 0 1 2 3
0 1 2 3 4 5 6 7 8 9
p r o c e s s i n g
p r o s s e s i n g
Note that only local computations and decisions are made
0

## Slide 87: Levenshtein distance - cont.
Finish filling in table
9 8 7 7 6 5 5 5 4 3
8 7 6 6 5 4 4 4 3 4
7 6 5 5 4 3 3 3 5 5
6 5 4 4 3 2 3 4 4 5
5 4 3 3 2 3 3 3 4 5
4 3 2 2 2 2 2 3 4 5
3 2 1 1 2 2 3 4 5 6
2 1 0 1 2 3 4 5 6 7
1 0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8 9
p r o c e s s i n g
p r o s s e s i n g
The global result is 3 !
So the Levenshtein distance is 3
0

## Slide 88: Levenshtein distance - end
Backtrack to find path actually taken
9 8 7 7 6 5 5 5 4 3
8 7 6 6 5 4 4 4 3 4
7 6 5 5 4 3 3 3 5 5
6 5 4 4 3 2 3 4 4 5
5 4 3 3 2 3 3 3 4 5
4 3 2 2 2 2 2 3 4 5
3 2 1 1 2 2 3 4 5 6
2 1 0 1 2 3 4 5 6 7
1 0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8 9
p r o c e s s i n g
p r o s s e s i n g
Remember:
The question is always how we got to a square
We see that the distance is 3
Since, e.g.,
substitution
insertion
deletion

## Slide 89: Generalization to DP
If not all substitutions are equally probable
  then we add the cost function instead of 1
We can also have costs for insertions and deletions
Di j = min ( Di-1 j + Ci-1 j; I j ; Di-1 j-1 + Ci-1 j-1; I j ; Di j-1 + Ci-1 j; I j )
And even more general rules are often used
This algorithm is called Dynamic Programming
and many other names
  Viterbi algorithm
  Levenshtein distance
  Dynamic Time Warping
but they are all basically the same thing!
The algorithm(s) are computationally efficient
  since they find a global minimum based on local decisions

## Slide 90: DTW
DTW uses the Dynamic Programming technique
for matching spoken words
The input is a feature vector (e.g., LPC, cepstrum)
and is separately matched to each dictionary word feature vector
  and the closest word is the winner!
The cost for each substitution needs to represent
how similar the two sounds sound
In isolated word recognition systems
  energy contours are used first to isolate the words
  linear time warping is then used to normalize the duration
  but special mechanisms are used for endpoint location flexibility
In connected word recognition systems
  the endpoint of each recognized utterance is used
  as a starting point for searching for the next word
In speaker-independent recognition systems
  multiple templates are used for each reference word

## Slide 91: Markov Models
An alternative to DTW is based on Markov Models
A discrete-time left-to-right first order Markov model
A DT LR second order Markov model
In Markov models future states depend only on the current state
What is the probability of remaining stuck in a state?
State 1 2 3 4
a11
a22
a33
a44
a12
a23
a34
probabilities
a12
a11
a22
a33
a44
a12
a23
a34
a13
a24
a11 + a12 = 1,
a22 + a23 = 1,
etc.
a11 + a12 + a13 = 1,
a22 + a23 + a24 = 1,
etc.

## Slide 92: Example
Which strings are possible? What are their probabilities?
ABCD p = 0.5*0.5*1 = 0.25
ABD p = 0.5 * 0.5 = 0.25
ACD p = 0.5 = 0.5
Note that the probabilities sum to 1 (of course!)
State A B C D
0.5
0.5
1
0.5
0.5

## Slide 93: Example
Which strings are possible?
ABCD
AABBCCDD
ABBBBBBBCD
ACBD
ABBCDCCD
AAAAA....
State A B C D
0.5
0.5
0.5
0.5
0.5
0.5
0.5
0.5
Which string is most probable?
What is its probability?
Which strings are 2nd most probable?
What are their probability?
What is the probability of an infinite string?

## Slide 94: Markov Models - cont.
General DT Markov Model
Model jumps from state to state with given probabilities
e.g. 1 1 1 1 2 2 3 3 3 3 3 3 3 3 4 4 4
or 1 1 2 2 2 2 2 2 2 2 2 4 4 4
1
2
3
4

## Slide 95: Markov Models - cont.
Why use Markov models for speech recognition?
  states can represent phonemes (or whatever)
  different phoneme durations (but exponentially decaying)
  phoneme deletions using 2nd or higher order
So time warping is automatic !
How do we use it?
We first build a Markov model for each word
Then, given an utterance
we select the most probable word

## Slide 96: HMM
But the same phoneme can be said in different ways
  so we need a Hidden Markov Model
a11
a22
a33
a44
a12
a23
a34
b11
b14
b12
b13
1
2
3
4
acoustic
phenomenon
aij are transition probabilities
bik are observation (output) probabilities
b11 + b12 + b13 + b14 = 1,
b21 + b22 + b23 + b24 = 1,
etc.

## Slide 97: HMM - cont.
For a given state sequence S1 S2 S3 … ST
the probability of an observation sequence O1 O2 O3 … OT
is P(O|S) = bS1O1 bS2O2 bS3O3 … bSTOT
For a given hidden Markov model M = { states, a, b }
the probability of the state sequence S1 S2 S3 … ST
is (the initial probability of S1 is taken to be pS1)
P(S|M) = pS1 aS1S2 aS2S3 aS3S4 … aST-1ST
So, for a given hidden Markov model M
the probability of an observation sequence O1 O2 O3 … OT
is obtained by summing over all possible state sequences

## Slide 98: HMM - cont.
P(O| M) = S P(O|S) P(S|M)
= S pS1 bS1O1 aS1S2 bS2O2 aS2S3 bS2O2 …
So for an observation sequence we can find
  the probability of any word model
(but this can be made more efficient using the forward-backward algorithm)
How do we train HMM models?
The full algorithm (Baum-Welch) is an EM algorithm
An approximate algorithm is based on the Viterbi (DP) algorithm
(Sorry, but beyond our scope here)

## Slide 99: The new world
DTWs and HMMs were the state of the art until recently
DTWs have little training time but long run times
HMM have long training times but short run times
Recently Deep Neural Networks have taken over many applications
DNNs
use essentially no knowledge about the speech signal
require astronomical amounts of data to train
have very long training times
provide no reasoning as to their decisions
can frequently outperform classical methods
but can also fail catastrophically
and can be subject to adversarial attacks

## Slide 100
Communications
signal processing

## Slide 101: Application: Data Communications
Communications is moving information from place to place
Information is the amount of surprise, and can be quantified!
Communications was originally analog – telegraph, telephone
There are many forms of digital communications that we use every day
Mobile (cellular)
  Internet
  from 4G voice is simply packet data
Television
  DVB (Idan plus)
  Cable TV (DOCSIS)
Home Internet access
  DSL (ADSL, VDSL)
  Cable modem (DOCSIS again)
Internet of Things
  smart home / smart city
  Industry 4.0

## Slide 102: Digital Communications
All physical channels
have limited bandwidth (BW)
add noise (so that the signal to noise ratio SNR is finite)
so analog communications always degrades
and there is no way to completely remove noise
In analog communications the only solution to noise
is to transmit a stronger signal
since later amplification amplifies N along with S
Communications has become digital
digital communications is all or nothing
  perfect reception or no data received

## Slide 103: Shannon’s Theorems
1. Separation Theorem
2. Source Encoding Theorem
Information can be quantified (in bits)
3. Channel Capacity Theorem
C = BW log2 ( SNR + 1 )
Warning: Shannon’s Laws are not constructive
they only give us targets to aim for!
source
encoder
channel
encoder
source
decoder
channel
decoder
channel
info
info
bits
bits
analog signal

## Slide 104: Modulation
We already learned that modulation means
changing parameters of a signal in order to carry information
We previously saw AM and FM in which
the signal carried analog information
Shannon leads us to ask how a signal can carry digital information
A simple example would be to modulate the amplitude of a DC signal
allowing it to be 0 or 1
We could also modulate the amplitude of a sinusoid (like in AM, but 0/1)
Since we will often need bidirectional transfer of information
it is convenient to package the modulator and demodulator
in a single box called a modem
(A similar box for analog modulation is called a transceiver)

## Slide 105: Digital communications
Shannon’s theorems taken together
explain why all communications has become digital
Analog communications always have quality degradation
Vinyl records are very limited in spectral and dynamic range
and add a tremendous amount of noise
A Compact Disk is essentially undistinguishable form the original
When recording from tape (e.g., cassette) to tape
each successive recording is noisier, until only noise remains
Copying CD to CD the 1000th copy is indistinguishable from the 1st
Scratching a CD/DVD, either there is no effect
or nothing works at all (in video there can be missing squares)

## Slide 106: The simple reason
Digital communications inherit a fundamental property of the bit
it is either 0 or 1 – on of off – perfect or nothing
Either you receive exactly what was sent
or you receive nothing (complete garbage)
But why is it perfect and not always nothing?
If I transmit a voltage of 3.14159... volt, but you receive 2.71828... volt
even if I tell you that there was noise and that isn’t what I sent
you can’t possibly figure out the right value
If I transmit a bit 1 and we obey Shannon’s laws
you should receive a bit 0
But even if you don’t and I tell you that you received the wrong value
then you know that the correct answer is 1 (error correction)

## Slide 107: Separation Theorem
The separation theorem is logically the first
even if chronologically the last
The theorem states that the optimal method of transporting
any kind of information (analog or digital) involves
  properly converting it into digital format (Shannon’s 2nd theorem)
  properly modulating an analog signal (Shannon’s 3rd theorem)
  recovering digital information from the received analog signal
  recovering original format information from the digital information
Note that
  the source decoder is the inverse of the source encoder
  input with the digital format it reproduces the original information
  the channel decoder is the inverse of the channel encoder
  input with the undistorted transmitted signal
  it reproduces the digital format information
  the channel encoder is designed with knowledge of the channel

## Slide 108: Channels
The problem with communications is that all physical channels
distort the signals traversing them
So that the signal received is not the same as the signal transmitted
Were it not for this distortion communications would be trivial
and there would be no limit on the possible (bit-)rate
From physics we know that all channels:
add noise (at least some dependent on temperature)
limit bandwidth (may be low-pass or bandpass)
with noise
bandwidth limited

## Slide 109: Information
What is information anyway?
Information is the amount of surprise
there is no information in yesterday’s newspaper
since we know everything and it doesn’t surprise us any more
Similarly, a constant sinusoidal signal carries no information
since it is deterministic – there is no surprise
This deterministic On/Off signal taking only 1 of two values
carries no information
But this one does carry information (it is stochastic - it surprises us!)

## Slide 110: Shannon’s bits
Shannon taught us that information can be quantified
You can compare the amount of information in a book
to that in a piece of music or in a picture
just like you can compare the weight of lead and feathers
The unit often used is the bit
Beware, Shannon’s bit is more general than Tukey’s binary digit
Tukey’s bit is only useful for encoding numbers
while Shannon’s bit can be used for any form of information
Consider the set of all items of interest
(e.g., all news items, all types of animals, all letters in an alphabet)
How much information is involved in selecting one item from this set?
Shannon’s bit is defined as follows:
ask questions with yes/no (binary) answers until you find out
the minimum number of questions required
is the information content in bits

## Slide 111: A simple example
Children play a game called 21 questions
One player (the puzzler) thinks of something – say an elephant
The other player (the questioner) asks yes/no questions
If he finds out in 21 questions or less the questioner wins
(and proves that the puzzler’s brain contains < 21 bits of information)
otherwise the puzzler wins
Is it an animal? YES
Is it bigger than a bread-box? YES
Does it live in the water? NO
Does it live in Africa? YES
Is it a lion? NO
Is it an elephant? YES
The questioner wins, but this is not the optimal set of questions
The optimal strategy asks questions
that divide the remaining possibilities in half!
(assuming equally probable items)

## Slide 112: When both bits are the same
When are Tukey’s bits the same as Shannon’s?
Assume that the set of all possibilities consists of the numbers
between 0 and 15
The puzzler thinks of the number 10
The questioner asks the optimal set of questions as follows:
Is greater than 7 ? YES = 1
Is greater than 11? NO = 0
Is it greater than 9 ? YES = 1
Is it greater than 10? NO = 0
So the Shannon information quantity is 4 bits
and the answers form the Tukey binary number for 10 – 1010
What should the questioner do if the items are not equally probable?
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15

## Slide 113: Source Encoding Theorem
What does this have to do with communications?
Shannon tells us that we need to first encode the information
according to Shannon’s 2nd law
Example: if the current letter in English text is Q
how much information is there in the fact
that the following letter is U?
Exactly zero! So we shouldn’t waste bits on it!
Example: assume a language with 4 letters A, B, C, and D
If they are all equally probable
then we can encode 00, 01, 10, 11 – 2 bits per letter!
But if p(A) = 1/2 p(B) = 1/4 p(C)=p(D)=1/8
how should we encode the letters?
A=1 B=01 C=001 D=000
Average bits per letter = 1/2*1 + 1/4*2 + 1/8*3 + 1/8*3 = 1.75 bits
This is smaller – and the minimal amount!

## Slide 114: Shannon information
We can generalize the last example
If we have N possible symbols, each of which has probability pi
then the information per symbols is given by
If we use the base-2 logarithm (physicists use ln and call this entropy)
we get the information in bits per symbol
If there are 2m equally probable symbols (each with p=2-m)
the information of selecting 1 symbol is (obviously) m bits
The information content of a string of K independent symbols
is K times the information of a single symbol
What is the entropy in bit/symbol of our previous example?
p(A) = 1/2 p(B) = 1/4 p(C)=p(D)=1/8
1/2 * log2(2) + 1/4 log2(4) + 1/8 log2(8) + 1/8 log2(8) = 1.75 bits/symbol

## Slide 115: Shannon encoding
Shannon’s 2nd law is not constructive –
it tells us how many bits are required to capture information
but doesn’t teach us how to actually encode information
So generations of mathematicians and engineers have developed
coding methods that approach Shannon’s information limit
Ziv and Lempel developed a digital file compression method
that approaches Shannon’s limit asymptotically (for large files)
the speech compression methods we already learned
are lossy methods of Shannon encoding for speech signals
the Joint Photographic Experts Group have developed
a lossy mechanism to encode images
the Motion Pictures Expert Group have developed
many lossy mechanisms for encoding video
If Ziv-Lempel compression can compress a file to 1/5 its size
why can’t we recompress that file to 1/25 the original?

## Slide 116: Error detection/correction
Information theory teaches us how to optimally encode information
and it also teaches us how to protect information from errors
You all know about parity bits
For example, we can add 1 bit to each byte making the number of 1s even
this adds 12.5% overhead
and detects any single bit error
but can’t correct any errors
Building on this we can make a simple error correction technique
that adds 16 bits to 64, i.e., 25% overhead
but can detect any two errors
and correct any single error
What happens if there two errors in the same row or column?
What happens if the error is in the parity check bits?
There are much more sophisticated error correction schemes!
01011001
01001010
00100000
01010011
01110100
01100101
01101001
01101110
0
1
1
0
0
0
0
1
01011001
01001010
00100000
01010011
01110100
01100101
01101001
01101110
0
1
1
0
0
0
0
1
01110110

## Slide 117: To FEC or not to FEC
Shannon’s separation theorem implies
that it is suboptimal to use data-layer Error Correction schemes
This is because an ECC always adds extra non-information bits
reducing the information bit rate
Yet, many communications systems use error detection/correction
CRC (Cyclic Redundancy Code) in Ethernet
turbo codes in cellular communications
Reed Solomon FEC in ADSL and optical networks
This is because unlike the assumptions of the capacity theorem
the SNR is often not stationary due to noise events and fading
resulting in errors in the recovered information
Signal layer ECC methods (e.g., TCM)
don’t contradict the separation theorem
source
encoder
ECC
encoder
source
decoder
ECC
decoder
channel
modulator
demodulator

## Slide 118: Channel capacity theorem
Shannon’s third theorem states that there is an upper limit
on the data rate in which bits can be transferred in a channel
This is the main reason a 100 Mbps Internet connection
costs more than a 20 Mbps one!
If there were no such limit then
why not give the customer as much as the routers can forward?
This capacity depends on
the Signal to Noise ratio
the amplitude of the modulated signal
divided by the amplitude of the noise added by the channel
the bandwidth of the analog channel (in Hz)
which is why communications people frequently say
bandwidth instead of data-rate!
Since this is a theorem in signal processing we are going to prove it
Well, actually our proof has a lot of holes
one day you should read Shannon’s real proof – just for the beauty of it!

## Slide 119: Channel Capacity (1)
Let’s first prove that a channel with no noise has infinite capacity
even if its bandwidth is close to zero
Let’s take some large amount of information
source encode it into bits 1011101001011110001010100010...
add “0.” at the beginning 0.1011101001011110001010100010...
to obtain a number between 0 and 1
place precisely that voltage as DC on the wire
connecting transmitter to receiver
since there is no noise precisely this voltage will be received
even though the bandwidth is small (DC requires no bandwidth!)
there is no physical limit on how fast this voltage can be measured
So we can transfer a large amount of data in negligible time
which means the capacity is infinite
XMTR
RCVR
v
t
0
1

## Slide 120: Channel Capacity (2)
1.5N
Now let’s prove that a channel with infinite bandwidth
has infinite capacity even if it has noise of peak-to-peak value N
Let’s take some large amount of information
source encode it into bits 1011101001011110001010100010...
for every 0 bit transmit 0 voltage for T seconds
for every 1 bit transmit 1.5N voltage for T seconds
for every 0 bit the receiver will see a voltage between –N/2 and N/2
for every 1 bit it will see a voltage between N and 2N
since there is no overlap the receiver can identify 0/1 with no error
since the bandwidth is infinite, we can send T→0
So we can transfer a large amount of data in negligible time
which means the capacity is infinite
N/2
-N/2
2N
0
N
DC-less noise with uniform distribution
N
-N/2
N/2

## Slide 121: Shannon’s capacity theorem
If there is both noise and limited bandwidth:
assume (wolg) that we transmit some signal with values between 0 and S
assume that the channel adds DC-less noise with uniform distribution
we’ll call the peak-to-peak noise N
so that the noise values are between –N/2 and +N/2
the receiver always sees values between –N/2 and S+N/2
so the receiver’s dynamic range is S+N
to maximize the information per symbol w/o overlap
we space the signal levels by N
so there can be (S+N)/N = S/N + 1 = SNR+1 different symbols
hence each symbol contains log2(SNR + 1) bits
but there can be BW symbols per second
Hence, the maximum information rate C = BW log2(SNR + 1) bit/s
The maximum spectral efficiency is C/BW = log2(SNR + 1) bit/s/Hz
N
S
0
S+N/2
-N/2
S+N
(S+N)/N
levels

## Slide 122: Capacity for frequency-dependent SNR
The capacity theorem assumed that the SNR was
constant from DC to BW
zero over BW
or more generally
constant in some passband
zero outside the passband
Which will not be the case if either
the signal attenuation (including multipath cancellation)
the noise (including interference)
or both, vary with frequency
The extension of the theorem is simple
divide the passband into channels of bandwidth Δf centered at f
the capacity theorem states that for the channel
Cf ≈ log2(SNR(f) + 1) Δf
the composite capacity is ∑f log2(SNR(f) + 1) Δf
The theorem becomes exact when we send Δf → 0
and then C = ∫ log2(SNR(f) + 1) df
SNR
f
BW
SNR
f
BW
0
Cf
f

## Slide 123: Water pouring theorem
The converse to Shannon’s channel capacity theorem
is Gallager’s water pouring theorem
The spectrum of the optimum (capacity-achieving) modulated signal
is given by the water pouring algorithm
fill a pitcher with a volume of water
  representing the total power to be transmitted
pour the water over the reciprocal SNR(f) graph (Noise to Signal Ratio)
This power spectrum can be achieved by
spectral shaping
explicit power loading
NSR
hi SNR – high transmitted power
very low SNR – no transmitted power
low SNR – low transmitted power

## Slide 124: Modem design
Shannon’s theorems are existence proofs
not constructive methods to design modulation techniques
that maximize capacity given channel characteristics
So we need to be creative to reach channel capacity
Over the years many kinds of modems have been designed :
NRZ
RZ
PAM
FSK
PSK
QAM
OFDM

## Slide 125: NRZ
Our first attempt is to simply transmit 1 or 0 (volts?)
This is called Non Return to Zero (i.e., NOT RZ)
Information rate = number of bits transmitted per second (bps)
But this is only good for short serial cables (e.g. RS232), because
requires DC (doesn’t work over radio or fiber)
if DC blocked lose runs of 1s
needs high bandwidth (sharp corners require high frequencies)
strong InterSymbol Interference
timing recovery may not be possible (if long runs of 0 or 1)

## Slide 126: NRZ needs infinite bandwidth
infinite BW
very low BW
and this is for 0101010101!
for random bits finite BW causes an additional problem!

## Slide 127: NRZ InterSymbol Interference (ISI)
insufficient BW to keep up with bit changes
low-pass filtered signal keeps up with bit changes

## Slide 128: DC-less NRZ
So what about transmitting -1/+1?
This is better, but not perfect!
DC isn’t exactly zero
if DC blocked worse than before
still is modulation of DC and not for fiber or radio
still has high bandwidth (sharp corners)
even without decay, long runs ruin timing recovery

## Slide 129: RZ
What about Return to Zero ?
never long + runs, so DC decay less important
BUT half-width pulses
  means twice the number of changes per second
  which requires twice the bandwidth!
Shannon strikes !

## Slide 130: OOK
Even better - use OOK (On Off Keying)
no signal discontinuity (but derivative discontinuities)
absolutely no DC!
based on desired sinusoid (“carrier”) frequency
so suitable for radio and fiber
can hear it (Morse code)

## Slide 131: NRZ - Bandwidth
The PSD (Power Spectral Density) of NRZ is a sinc (sinc(x) = sin(x)/x)
the first zero is at the bit rate (from the uncertainty principle!)
so channel bandwidth limits bit rate
DC depends on level placement (may be zero or spike)

## Slide 132: OOK - Bandwidth
PSD of -1/+1 NRZ is the same, except there is no DC component
If we use OOK the sinc is mixed up to the carrier frequency
(The spike helps in carrier recovery)
fc

## Slide 133: From NRZ to n-PAM
NRZ
4-PAM
(2B1Q)
8-PAM
Each level is called a symbol or baud
Bit rate = number of bits per symbol * baud rate
+3
+1
-3
-1
11
10
01
01
00
11
01
111
001
010
011
010
000
110
GRAY CODE
10 => +3
11 => +1
01 => -1
00 => -3
GRAY CODE
100 => +7
101 => +5
111 => +3
110 => +1
010 => -1
011 => -3
001 => -5
000 => -7
+1
-1
1
1
1
0
0
1
0

## Slide 134: PAM - Bandwidth
BW (actually the entire PSD) doesn’t change
with the number of levels !
So we should use many bits per symbol
But then noise becomes more important
(Shannon strikes again!)
BAUD RATE

## Slide 135: ASK
What about Amplitude Shift Keying - ASK ?
2 bits / symbol
generalizes OOK in the same way that PAM generalized NRZ
not widely used since hard to differentiate between levels
when there is noise
How do we find the amplitude of a sine?

## Slide 136: FSK
What can we do about noise?
If we use frequency diversity we can gain 3 dB
Use two independent OOKs with the same information
(no DC)
This is FSK - Frequency Shift Keying
We maintain continuous phase for minimum bandwidth
Note that sinusoids are orthogonal – but only over long times !

## Slide 137: FSK in the frequency domain
FSK is based on orthogonality of sinusoids of different frequencies
make decision only if there is energy at f1 but not at f2
The uncertainty theorem says that the uncertainty in frequency
is inversely proportional to the time duarion
So when we leave a frequency for a short amount of time
its spectrum is not a line – but a sinc!
So FSK is robust but slow (Shannon strikes again!)

## Slide 138: PSK
What about sinusoids of the same frequency but different phases?
Correlations reliable after a single cycle (∫sin(ωt) cos(ωt) dt = 0 on 1 cycle!)
So let’s try BPSK
1 bit / symbol
or QPSK
2 bits / symbol
Bell 212 2W 1200 bps
V.22

## Slide 139: QAM
Finally, we can combine PSK and ASK (but not FSK)
by changing both the amplitude and the phase
2 bits per symbol
This is called Quadrature Amplitude Modulation
This is getting confusing

## Slide 140: The secret math behind it all
Remember the Hilbert Transform?
x(t) = A(t) cos ( 2 p fc t + f(t) )
y(t) = A(t) sin ( 2 p fc t + f(t) )
A(t) is the instantaneous amplitude, f(t) is the instantaneous phase
This can be used to demodulate analog/digital communications signals
For digital modulations we draw constellation diagrams
x and y as axes
A is the radius, f the angle
For example, QPSK can be drawn (rotations are time shifts)
Each point represents 2 bits!

## Slide 141: QAM constellations
16 QAM V.29 (4W 9600 bps)
V.22bis 2400 bps Codex 9600 (V.29)
2W
first non-Bell modem (Carterphone decision)
Adaptive equalizer
Reduced PAR constellation
Today - 9600 fax!
8PSK
V.27
4W
4800bps

## Slide 142: Voicegrade modem constellations

## Slide 143: Spectral efficiency of modulations
We defined spectral efficiency as the bit/s per Hz
We can now compare the modulation techniques we have seen so far
Note that we are using raw (DSB) efficiencies
values for PSK and QAM can be improved by a factor of 2 !
modulation | bit/symbol | BW/symbol rate | spectral efficiency
NRZ | 1 | 1 | 1
BPSK | 1 | 2 | 0.5
QPSK | 2 | 2 | 1
8PSK | 3 | 2 | 1.5
16QAM | 4 | 2 | 2
64QAM | 6 | 2 | 3
256QAM | 8 | 2 | 4

## Slide 144: FDM
QAM (including PSK as a special case) is a very efficient modulation
approaching the Shannon capacity for simple bandpass channels
But the spectrum of a QAM signal is inflexible
like all discretely keyed modulations of a single carrier
it is a sinc centered at fc with first zeros at fc ± symbol-rate
The spectrum can be shaped using a Tomlinson precoder
but this requires a feedback channel and precomputing the filter
So, QAM does not lend itself to water-pouring
The trick is to use Frequency Domain Multiplexing
We saw FDM as a technique to mux different information sources
Here we divide a single information stream into blocks of bits
and mux them together using distinct sub-carriers
Each sub-carrier signal can
have its own power level
use its own modulation technique (PSK, QPSK, 16QAM, 64QAM, ...)
thus directly implementing water pouring

## Slide 145: FDM combats ISI but creates ICI
FDM uses many subchannels, each with low bandwidth but low data rate
Since the data rate is low, there is essentially no ISI
And since each subchannel is localized in frequency
we can perform equalization in the frequency domain (FEQ)
i.e., simply multiply each frequency and shift its phase
But, we need to space the sub-carriers far enough apart
to avoid InterChannel Interference
This squanders bandwidth, distancing us from the Shannon capacity

## Slide 146: OFDM
The solution is called Orthogonal FDM (OFDM)
all sub-channels use the same symbol rate (even if different modulations)
sub-carriers are spaced at precisely the symbol rate
the sub-carriers are the precisely orthogonal
  and hence do not interfere with each other
ICI is eliminated with no guard frequencies needed
simple implementation based on the FFT

## Slide 147: Why are the channels orthogonal?
Let’s look at the baseband signal
where all sub-carriers are multiples of the symbol rate
so that there are an integral number of sinusoid cycles in a symbol
Any two such signals are precisely orthogonal
= 0 (the only requirement is for a whole number of cycles of sin Δω t !)
and the same is true if we arbitrarily phase shift or amplify the signals

## Slide 148: Spectral efficiency
OFDM provides the minimum possible sub-carrier spacing
and hence eliminates the need for guard bands
Now each sub-channel effectively occupies only symbol-rate of bandwidth
So the spectral efficiencies improve by a factor of 2 !
modulation | bit/symbol | BW/symbol rate | spectral efficiency
BPSK | 1 | 1 | 1
QPSK | 2 | 1 | 2
8PSK | 3 | 1 | 3
16QAM | 4 | 1 | 4
64QAM | 6 | 1 | 6
256QAM | 8 | 1 | 8

## Slide 149: FFT
In order to transmit each sub-channel
we should modulate a baseband signal
up-mix each to the desired sub-carrier frequency (multiply by )
and add the sub-channels together
The upmixing can be performed in parallel for all sub-carriers
by the inverse Fourier transform (Zimmerman and Kirsch 1967)
and the FFT does it quickly (Weinstein and Ebert 1969)
sin(ω1t)
sin(ω2t)
modulator
sin(ω3t)
.
.
.
modulator
modulator
serial to parallel converter
bit
stream
D/A
analog signal

## Slide 150: OFDM modem paradigm
.
.
.
modulator
modulator
modulator
modulator
modulator
modulator
modulator
modulator
IFFT
bit
stream
bit allocation
.
.
.
demodulator
FFT
demodulator
demodulator
demodulator
demodulator
demodulator
demodulator
demodulator
bit
stream
channel
transmitter
receiver
parallel to serial bit converter
D/A
A/D
WARNING
this is not quite correct yet !
framer
deframer

## Slide 151: Cyclic prefix
What we previously derived almost works
For analog digital signal processing
linear cyclic convolution in the time domain y = h * x
is equivalent to multiplication in the frequency domain
So, the linear convolution in the analog channel
has to be converted into cyclic convolution for the digital channel
This is done by adding a Cyclic Prefix to the signal
which basically acts as a guard interval to eliminate ISI
The CO duration tends to be from 1/32 up to 1/4 of the symbol duration
and has to be long enough to include the maximum ISI spread
For example, if ISI is due to multipath
then the CP must be long enough to incorporate the longest delayed path
Yk = Hk Xk
Y(ω) = H(ω) X(ω)
OFDM symbol = output of IFFT
CP
CP length

## Slide 152: CP at work
OFDM splits the signal in the time domain into frames
In order for the signal processing of each frame to be independent
the CP ensures that delay spread is within the received frame
As a simple example, assume a frame of 8 samples
a 2-sample multipath yn = xn + h1 xn-1 + h2 xn-2 and CP of 2 samples
The OFDM frame before CP insertion is x0 x1 x2 x3 x4 x5 x6 x7
After CP insertion the xmted OFDM frame is x6 x7 x0 x1 x2 x3 x4 x5 x6 x7
The received OFDM signal is y6 y7 y0 y1 y2 y3 y4 y5 y6 y7
where y6 and y7 contain ISI from the previous frame and are discarded
and
All the information is present for equalization to recover the original x0 ... x7
and the matrix is circulant – which is solved in the frequency domain!

## Slide 153: 4G OFDM signal structure
f
t
GUARD BAND
GUARD BAND
sub-carrier
OFDM symbol
For 4G:
channel bandwidth ..., 5, 10, 15, or 20 MHz
guard band overhead is 10%
sub-carrier spacing = 15 kHz
OFDM symbol duration = 1/15KHz = 66.67 μsec
  short CP = 4.7 μsec so total duration = 71.367 μsec
    1 slot = 7 symbols ≈ ½ msec*
  long CP = 16.7 μsec so total duration = 83.367 μsec
    1 slot = 6 symbols ≈ ½ msec*
* CP durations are adjusted so that the slot is precisely ½ msec
BW (MHz) | usable BW (MHz) | subchannels | FFT
5 | 4.5 | 300 | 512
10 | 9 | 600 | 1024
15 | 13.5 | 900 | 1536
20 | 18 | 1200 | 2048

## Slide 154: OFDM modem
bit
stream
interleaving and FEC
bit
allocation
IFFT
CP
insertion
D/A
upconversion
downconversion
bit
serializer
FFT
CP
removal
A/D
FEQ
modulators
demodulators
bit
stream
FEC
framer
deframer
antialisasing
filter
power
amplifier
Warning: this is somewhat over-simplified!

## Slide 155: OFDMA
4G and 5G cellular are based on OFDM
but need Multiple Access and Duplexing mechanisms too
For MA an orthogonal version of FDMA is used
signals from/to different users occupy different frequencies
the SubCarrier Spacing must be exactly the OFDM symbol rate
For duplexing there are two alternatives:
Frequency Domain Duplexing
different frequency bands are used for the UL and DL
for example n1: UL 1920-1980 MHz, DL 2110-2170 MHz
Time Domain Duplexing
a single frequency band is used
for example n38: 2570-2620 MHz for both UL and DL

## Slide 156: OFDMA
The basic OFDM paradigm can be readily extended to OFDMA
by allocating time-frequency Resource Elements to different users
In the DL direction the base-station transmits to all users
and each needs to know which REs it needs to extract
In the UL direction each UE transmits only in its REs
in order not to interfere with other UEs in the cell
f
t
GUARD BAND
GUARD BAND
Resource
Element
SCS
symbol

## Slide 157
Financial signal processing

## Slide 158: Application : Stock Market
This signal is hard to predict (extrapolate)
self-similar and fractal dimension
polynomial smoothing leads to overfitting
noncausal MA smoothing (e.g., Savitsky Golay) doesn’t extrapolate
causal MA smoothing leads to significant delay
AR modeling works well
  but sometimes need to bet the trend will continue
  and sometimes need to bet against the trend