## Slide 1: TSN
Yaakov (J) Stein

## Slide 2: Time sensitive (deterministic) flows
Communications for some applications (see draft-ietf-detnet-use-cases)
require deterministic or time-sensitive handling
professional video and audio (e.g., intra-studio, broadcast, public address)
critical infrastructure supervisory control (e.g., IEC 61850)
building automation systems
industrial M2M (e.g., 802.15.4e, 6TiSCH)
vehicle to vehicle (V2V) and vehicle to infrastructure (V2I) communications
cellular fronthaul and backhaul
blockchain pools
Common requirements
high availability (> 5 nines)
guaranteed message delivery
rapid response times
consistent response times
precise timing
synchronized actions
human interaction

## Slide 3: 5G URLLC
When defining the 5th generation of mobile networks
ITU and 3GPP decided to define three vertical market segments
enhanced Mobile Broadband (eMBB)
initial deployments
higher data rates and moderate latency improvement
requires New Radio and larger backhaul pipes
massive Machine Type Communications (mMTC)
low power wide area (LPWA) technologies, including NB-IoT
enhancements to Release 13/14 features
Ultra Reliable Low Latency Communications (URLLC)
final stage
mission/life critical applications
ultra-reliable low end-to-end latency
requires 5G Core deployment

## Slide 4: TSN background
Time Sensitive Networking (TSN) and Deterministic Networking (DetNet)
are Ethernet and IP/MPLS technologies that enable:
very low and guaranteed packet propagation latency
  time aware scheduling/queuing
  time coordinated forwarding
  frame preemption
very high reliability
  zero congestion loss (PLR of 10-10)
  resource reservation
  seamless redundancy
dynamicity – flows can be removed or added w/o impacting other flows
co-existence of TSN traffic with regular traffic
  up to 75% express traffic
for applications such as IIoT, V2x, fronthaul
TSN is being developed for Ethernet by a task group in IEEE 802.1
The same technologies are being developed for IP and MPLS
by the DetNet WG in the IETF

## Slide 5: Why latency?
Some applications require very low latency
interactive audio/video
Virtual Reality / Augmented Reality
mobile fronthauling
algotrading
critical infrastructure (e.g., teleprotection)
remote jamming
Some applications require deterministic latency
enables synchronizing industrial devices
enables synchronizing data streams (e.g., lip synching)
facilitates distributed power generation
translates to efficiency
can be translated to zero congestion
Bounded delay can be converted to deterministic delay
by adding a compensation buffer

## Slide 6: Why very low PLRs?
While Internet Packet Loss Ratios can approach 1%
and cellular air interface induces much worse
Carrier Ethernet can give PLRs of 10-6 !
Why do we need any better than that?
Example 1 : industrial failures
assume that 2 consecutive packets lost to a machine in a factory
may cause the machine to jam, halting production
GbE may sustain 1.5 Mpps, or about 1011 packets per day
  so a factory with 10 operational networks handles 1012 packets per day
a PLR of 10-6 under IID means a 2-packet loss ratio of 10-12
  so there will be a production halt every day!
Example 2 : audio-video mastering
mastering an 8K (7680*4320) at 60 fps requires 3.8GBps = 2.5 Mpps
a camera to storage PLR of 10-6 this means 2.5 packet losses per second!
since latency rules out TCP, recording is impossible

## Slide 7: QoS in 802.1
802.1 defines several QoS mechanisms
Traffic Class (802.1Q-2014 Annex I)
multiple queues per port and strict/WF queuing
congestion notification (CNM – 802.1Q 33.3)
EFM OAM (802.3 clause 57)
Connectivity Fault Management (802.1Q 19)
and other SDOs have defined traffic conditioning mechanisms
But traditional Ethernet specifications
do not directly address guaranteeing QoS for real-time traffic
This led to the formation of the
802.1 Audio-Video Bridging Task Group
PCP | TC
0 | background
1 | best effort
2 | excellent effort
3 | critical application
4 | video <100 ms
5 | voice <10 ms
6 | Internetwork control
7 | control data

## Slide 8: 802.1 AVB history
2003 Metcalfe challenged the Ethernet community to address new media
such as networked home entertainment
July 2004 IEEE 802.3 issued a Call for Interest, relating to
application of Ethernet to time sensitive consumer Audio/Video Devices
time/phase sensitive applications
new networking requirements created by digital media
November 2005 work moved to IEEE 802.1 - Residential Ethernet SG
which later became the Audio Video Task Group
The AVB task group produced 4 deliverables:
IEEE 802.1BA: Audio Video Bridging (AVB) Systems
IEEE 802.1AS: Timing and Synchronization for Time-Sensitive Applications (PTP profile)
IEEE 802.1Qat: Stream Reservation Protocol (SRP)
IEEE 802.1Qav: Forwarding and Queuing for Time-Sensitive Streams (FQTSS)
2012 the AVB Task Group morphed into the TSN Task Group

## Slide 9: 802.1 AVB targets / enhancements
AVB was tasked with enhancing 802.1 bridges to achieve:
2 ms guaranteed latency through 7 Ethernet bridges
admission control (reservations) for guaranteed bandwidth
precise synchronization for timestamps and media coordination
  < 1µs absolute synchronization between devices
  jitter less than 100ns, filterable down to 100ps
  to meet the MTIE mask for professional uncompressed video
It achieved this by enhancing 802.1Q, 802.3, 802.11, in particular:
traffic shaping and prioritizing (802.1Qav)
admission control (MMRP and SRP, 802.1Qat)
synchronization based on a profile of 1588 (802.1AS)

## Slide 10: IEEE 802.1 TSN history
During 2005-2012 the Audio Video Bridging (AVB) Task Group
addressed time sensitive Ethernet for the AV market (pro and consumer)
In 2012 the TG was renamed TSN to handle other use cases
including industrial, infrastructure, transportation, aerospace, fronthaul
TSN fundamental principles
assume highly accurate synchronization of bridges (better than 1 μsec)
provided by the 802.1AS profile of IEEE 1588
utilize protocol for reservation of resources (buffers, BW on links)
achieve bounded latency for time sensitive streams
  new time-based buffering/queuing mechanisms
  frame pre-emption
achieve very low PLR (better than 10-6)
  zero loss due to congestion due to new queuing and shaping mechanisms
  seamless redundancy by 1+1 replication + elimination
must support co-existence of critical and BE traffic in the same network
(even when critical traffic is 75%)

## Slide 11: TSN task group in 802
802
802.1
802.3
IEEE
IEEE-SA
RevCom
NesCom
PatCom
802.11
802.15
Standards Board
Board of Governors
. . .
DCB TG
Maintenance TG
TSN TG
OmniRAN TG
Security TG
802.1Qbu 802.1Qbv 802.1CB ...

## Slide 12: TSN Components (some already in 802.1Q-2018)
Latency
802.1Qav (clause 34) Forwarding and Queuing Enhancements
802.1Qbu, 802.3br Frame preemption
802.1Qbv Scheduled traffic
802.1Qch (Annex Q) Cyclic queuing and forwarding
802.1Qcr Asynchronous shaping
Reliability
802.1CB (standalone) Frame Replication and Elimination
802.1Qca Path control and Reservation
802.1Qci Per-stream filtering and policing
802.1AX-rev LAG revision
Resource Management
802.1Qat (clauses 34, 35) Stream reservation protocol (SRP)
802.1Qcc SRP enhancements and performance improvements
802.1Qcw Yang data models for Qbv, Qbu, and Qci
802.1CS Link local reservation protocol
Misc
802.1AS Timing (including 1588 profile)
802.1CM TSN for mobile fronthaul
IEEE 1722 Layer 2 Transport Protocol for TSN

## Slide 13: TSN latest status
Project | Subject | Current stage | Draft #
802.1Qbu | Frame preemption | Published | 3.1
802.1Qbv | Scheduled traffic | Published | 3.1
802.1Qbz | 802.11 Bridging | Approved | 2.4
802.1Qca | IS-IS Path Control and Reservation | Published | 2.1
802.1CB | Frame Replication and Elimination | Sponsor Ballot | 2.8
802.1Qcc | SRP enhancements & performance improvements | WG ballot | 1.5
802.1Qch | Cyclic queueing and forwarding | Published | 2.2
802.1AS/Cor2 | Tech and editorial corrections | Approved | 3.0
802.1AS-REV | Time synch enhancements | WG ballot | 5.0
802.1Qci | Per Stream Filtering & Policing | Approved | 2.0
802.1Qcj | Auto Attach to PBB | Editor's draft | 0.2
802.1CM | Profile for Fronthaul | TG Ballot | 0.7
802.1Qcp | 802.1Q YANG data model | WG ballot | 1.1
802d | URN Namespace | Published | 1.2
802.1Qcr | Asynchronous Traffic Shaping | Editor's draft | 0.1
802.1CS | LRP (new registration protocol) | Editor's draft | 0.1
802.1Q-REV | Bridges and Bridged Networks | WG ballot recirc | 2.0
802.1CBcv | FRER YANG & MIB | develop PAR | 
802.1Qcw | TSN (Qbu, Qbv, Qci) YANG | develop PAR | 

## Slide 14: IETF DetNet WG
July 2015 DetNet held a BoF session at IETF 93
proposing the formation of a WG to address
multi-hop paths with deterministic properties
  controlled latency
  low packet loss
  ultra-low PDV
  high reliability
deterministic flows for IPv4, IPv6, MPLS
  mechanisms to reserve/release resources
  encapsulations
  forwarding behaviors
  YANG models
compatibility with TSN work
October 2015 DetNet WG was chartered

## Slide 15: DetNet Drafts (Works in Progress)
The DetNet WG has the following active IDs:
draft-ietf-detnet-architecture DetNet Architecture
draft-ietf-detnet-dp-sol-ip DetNet IP Data Plane Encapsulation
draft-ietf-detnet-dp-sol-mpls DetNet MPLS Data Plane Encapsulation
draft-ietf-detnet-flow-information-model DetNet Flow Information Model
draft-ietf-detnet-problem-statement DetNet Problem Statement
draft-ietf-detnet-security DetNet Security Considerations
draft-ietf-detnet-use-cases DetNet Use Cases
draft-ietf-detnet-yang DetNet Configuration YANG Model

## Slide 16: DetNet Related Drafts (Eo2018)
draft-chen-detnet-loss-delay Packet Loss and Delay PM
draft-chen-detnet-sr-based-bounded-latency SR-based Bounded Latency
draft-finn-detnet-bounded-latency Bounded Latency
draft-geng-detnet-info-distribution IGP-TE Extensions
draft-geng-detnet-requirements-bounded-latency Large-scale DetNet delay
draft-huang-detnet-single-path-pref Single-path PREF
draft-jiang-detnet-ring DetNet in Ring Topologies
draft-mirsky-detnet-oam DetNet OAM
draft-qiang-detnet-large-scale-detnet Large-Scale DetNet scalability
draft-wang-detnet-backhaul-architecture
Joint Scheduling Architecture for Industrial Field/Backhaul Networks
draft-xiong-detnet-qos-policy DetNet QoS Policy
draft-xiong-detnet-qos-yang DetNet QoS Yang

## Slide 17: Theoretical Note
Much of the TSN/DetNet work is based on the Network Calculus
a mathematical theory dealing with deterministic queuing
such as in communications networks
Network Calculus enables computation of bounds
on queuing delays, buffer sizes, burstiness, etc.
and then to combine them
into end-to-end properties
thus providing formal delay guarantees
Network calculus also enables
design and analysis of various mechanisms such as shapers

## Slide 18: 802.1Qbu Frame preemption
The major source of residence latency for a high priority packet
is its waiting in a queue for a packet being output to complete transmission
For example, assuming a 1500 B packet just started transmission
the high priority packet needs to wait:
10 Mbps 1.7 msec
100 Mbps : 170 msec
1 Gbps : 17 msec
10 Gbps 1.7 msec
100 Gbps 0.17 msec
and the situation will be much worse with 9K jumbo packets
which are being standardized
It is possible with present protocols to runt the outgoing packet
but this would require its retransmission
and burden switches along the path to parse and discard it
A solution to this problem (not the most important element in TSN!)
involves preemption, frame fragmentation, and local reassembly

## Slide 19: 802.1Qbu Frame preemption
Published in 2016 and being absorbed into 802.1Q
When express frame(s) arrives and a normal frame is being transmitted
the packet transmission of the normal frame is temporarily suspended
the neighboring switch buffers the content received
the express frame(s) are sent and forwarded
the transmission of the normal frame is continued
the neighboring switch reassembles the outgoing packet and forwards
Optimal bandwidth utilization of background traffic for time aware shaping and low-latency communication in non-scheduled networks

## Slide 20: 802.3br Interspersing Express Traffic (IET)
802.3br provides Ethernet physical layer support for frame preemption
All frames are classified as either express or preemptable
Frame could be preempted multiple times
but no nested preemption
IET support is discovered via LLDP (new TLV)
Express frames have the usual preamble
but a special physical start-of-frame
SMD-e = 55 instead of SFD = AB
Frame fragments
are at least 64 bytes (multiple of 8 except last fragment)
have usual preamble but special start-of-frame
  first fragment has SMD-Ix = 66 CC FF 33 (for frame 0 1 2 3)
  non-initial fragments have SDM-Cx = E1 D2 1E 2D + fragment ctr
have a 0..3 fragment counter
have their own (modified) FCS
are not valid MAC frames for non-compliant devices
802.1Qbu
802.3br

## Slide 21: 802.1 (not MEF!) Queuing
802.1Q-1988 defined strict priority selection
802.1Qaz (absorbed into 802.1Q-2012)
added weighted queues
802.1Qat adds credit-based fair queuing
(borrowed from RPR)
transmit frames when non-negative credit
credit increases when frames wait
802.1Qbv adds time-sensitive queues
queues are Open or Closed
according to timeslots
priority selector
priority selector
weighting
priority selector
weighting
priority selector
weighting

## Slide 22: 802.1Qat Credit Based Queuing
802.1Qat adds credit-based fair queuing (borrowed from RPR)
a Credit Based Shaper (CBS) spaces out frames to reduce bunching / bursting
a frame is only transmitted when its queue has non-negative credit
credit
  increases at rate idleSlope when frames are waiting
  or no frames waiting but credit is negative
  decreases at rate sendSlope when frames are transmitting
  rates are adjustable (per queue results in weighted queuing behavior)
shaped queues have highest priority (higher than unshaped queues)
Qat still guarantees bandwidth to the highest unshaped priority
CBS is similar to burst rate shaper
but with useful mathematical properties
  only parameter is bandwidth
  impact on queue of adjacent shapers = impact of 1 shaper with total BW

## Slide 23: CBS example

## Slide 24: 802.1Qbv Scheduled Traffic
Published in 2015 and being absorbed into 802.1Q
Qbv introduces Time Aware Traffic Shaping (Time Sensitive Queues)
requires that every network element
  has highly accurate time (e.g., from 1588)
time-gated egress CoS queues transmit one at a time
based on a precise timeslot schedule
implemented by circular collection of time aware gates
Directly timing release of packets can
support scheduled applications (e.g., process/vehicle control)
provide latency and PDV guarantees
completely avoid congestion
return to TDM-like determinism
Qbv retains credit-based shapers for non-scheduled applications

## Slide 25: Time Sensitive Queues
In Qbv all CoS queues (not just the TSN queues) are cyclically gated
so non-TSN traffic is also released in timeslots
Qbv generally results in bursts of packets belonging to a stream
Timeslot schedules are dynamically computed
by a centralized management system
that configures the network nodes using SRP
Schedules are specified with up to 1 ns granularity
(although implementations may be less precise)
thus PDV can be reduced to about 1 ns
Schedules might require guard times between TSN timeslots
unless preemption is used

## Slide 26: Qbv Scheduler
T |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 |  | O | C | O | O | C | O | O | O
1 |  | C | O | O | O | O | O | C | C
2 |  | O | C | C | C | C | O | O | O
3 |  | O | O | O | O | C | C | C | O
N | repeat |  |  |  |  |  |  |  | 
selector
Gate Schedule
0
1
2
3
4
5
6
7
gates
CoS queues
PCP

## Slide 27: 802.1AS-REV
How do we synchronize all the network elements ?
In general, TSN assumes that all time sensitive elements
are sync’ed to a PTP-synchronized clock
802.1AS (produced by AVB TG) is a profile of IEEE 1588
The new revision of 802.1AS includes enhancements:
multiple synchronization domains
common peer delay for multiple domains
support for 802.11 Fine Timing Measurement (FTM)
support for 802.1AX LAG
improved scalability
support for 1588 1-step
improved support for long chains, rings
more responsive
faster GM change over
reduced BMCA convergence time
configure redundant paths and redundant GMs

## Slide 28: Peristaltic Queuing
What can we do with Qbv time-gated queues?
Knowing in detail each scheduled flow’s behavior
we could configure every NE in the entire network
to be free precisely when the next scheduled packet arrives
(this can be done using 802.1Qav)
But there is a simpler (but less optimal) method
called peristaltic queuing

## Slide 29: 802.1Qci/Qch Cycling Queuing
802.1Q-2018 Annex Q (CQF, formerly called peristaltic shaping)
Exploits accurate timing to provide without intricate signaling
defined (nonoptimal) upper latency bound
Each switch collects frames according to PCP
and forwards all packets of the same traffic class in one cycle
Maximum bytes allowed per clock cycle configured by SRP

## Slide 30: 802.1Qat SRP
Stream Reservation Protocol is similar to RSVP or RSVP-TE
in that it reserves network resources for flows
and uses a Traffic Specification (Tspec)
802.1Qat published in 2010, absorbed into 802.1Q-2011
SRP is used to configure all of the TSN features
SRP is based on the Multiple Reservation Protocol (802.1Qak)
like MVRP (Multiple VLAN Registration Protocol) and
MMRP (Multiple MAC Registration Protocol)
SRP specifies the required resources and enables their dynamic maintenance
and facilitates registration, deregistration, and retention
of resource reservation information in relevant network elements
• Talker Declarations are distributed along the path(s) to Listeners
• Listener Declarations run back and actually reserve resources

## Slide 31: 802.1Qcc SRP
802.1Qcc proposes enhancements to SRP as defined by Qat
support for 1000s of streams
configurable SR (stream reservation) classes and streams
reduce chattiness
reduce CPU load for handling SRP
supports L2
but probably won’t support L3 (DetNet) streaming (IETF has other protocols)

## Slide 32: 802.1Qav FQTSS
Forwarding and Queuing Enhancements for Time-Sensitive Streams
Approved by AVB TG in 2009 and is now clause 35 of 802.1Q-2014
planning and admission control (CAC) based on SRP
procedures for mapping priorities to traffic classes
  class A - latency ≤ 2 msec
  class B - latency ≤ 50 msec
  control traffic (AS and SRP)
  best effort traffic
precise synchronization based on 802.1AS
CBS shaping of streams at source based on 802.1Qat
identification of non-participating devices

## Slide 33: 802.1Qcr Asynchronous Traffic Shaping
New project ATS
Define an asynchronous mechanism (w/o sync’ed nodes)
for constant bit data rates and full-duplex links
better than CBS
Bounded delays/lossless for conformant flows
even in presence of non-conformant flows
2 proposals - both intermediate between CBS and CQF
paternoster algorithm
ATS algorithm

## Slide 34: 802.1CB Frame Replication and Elimination
Published in 2017 Frame Replication and Elimination for Reliability
Basically a packet-by-packet 1+1 protection mechanism
no failure detection needed
insert stream ID and sequence number into every FRER frame
frames are replicated at source
duplicates are eliminated at destination
Several stream identifier methods:
DA + VID
SA + VID
DA + VID + IP SA + IP DA + DSCP + ...
Several sequence number methods:
new L2 sequence number tag for Ethernet frames
HSR or PRP sequence numbers
Ethernet PW sequence numbers

## Slide 35: Re-replication and Re-elimination
But replicating at source and eliminating at destination
only protects against a single network failure
(except source and destination points themselves, which are out of scope)
FRER allows configuring replication and elimination
at intermediate nodes
replicate
replicate
eliminate
eliminate
replicate
eliminate

## Slide 36: FRER Reordering
802.1CB does not require in-order delivery
because it assumes that there are large buffers
and packets can be re-ordered
802.1CB distinguishes between :
intermittent flows (e.g., SCADA)
  time between packets > Δ end-to-end latencies
  simple elimination algorithm - discard if SN isn’t > last SN
bulk flows (e.g., video streams)
  many more packets in flight on one path than another
  need to remember multiple SNs

## Slide 37: 802.1Qca Path control and reservation
Published in 2015 and being absorbed into 802.1Q
Defines IS-IS extensions
to enable the multiple paths required by 802.1CB FREF
Redundancy paths are computed
and distributed throughout the network
Paths can be completely (explicitly) pinned
or loosely pinned (only to certain points)
Paths can be specified using metrics
not usually used for forwarding
Includes algorithms for finding multiple maximally disjoint paths
according to various criteria

## Slide 38: 802.1Qci Per Stream Filtering/Policing
Published in 2017
Enables gating and metering (policing) on a per-stream basis
called Per Stream Filtering and Policing (PSFP)
in order to protect against
excess bandwidth usage
burst sizes
faulty/malicious endpoints
Operations are based on
stream ID and priority
filters
meter ID and frame counters
Flow metering should be based on MEF 10.3 dual token buckets
(without envelope and rank) but with some new features
Gating holds packets
while metering marks, and optionally drops them
queuing frames
...
egress filtering
stream gates
flow meters
stream filters

## Slide 39: 802.1CM Time-Sensitive Networking for Fronthaul
Published in 2018
Joint work with the CPRI Cooperation
Specifies requirements for transporting time-sensitive fronthaul streams over Ethernet networks
including delay and sync (with calculations)
Specified for CPRI (class 1) [encapsulation not specified]
and eCPRI (class 2)
CPRI flows (IQ data, C&M control/management, sync)
are handled as separate flows
Synchronization via SyncE and ITU-T telecom profile (BC or TC)
Adopts eCPRI’s categories (A+, A, B, C)
and specifies 2 profiles

## Slide 40: 802.1CM Profiles
Profile A
use legacy Ethernet equipment
strict priority Ethernet bridge
  IQ data with high priority traffic class
  C&M data with lower priority
use 2000 bytes for all frames
MEF 10.3 shaping
Profile B
assume very minimal TSN functionality is present
Qbu+3br preemption enabled bridge
  IQ data is express traffic
  C&M data is preemptable
2000 bytes frames for IQ frames, flexible for others
MEF 10.3 shaping

## Slide 41: Thanks for listening