## Slide 1: Ethernet vs. MPLS-TP in Access Networks
The Access Company
Presented by:
Yaakov (J) Stein
CTO

## Slide 2: What is this talk about ?
Ethernet is the packet technology
that dominates access networks today
MPLS-TP is threatening to replace Ethernet in these networks
Is MPLS-TP up to the task ?
Is MPLS-TP ready ?
I start with a brief review of
characteristics of access networks
characteristics of Ethernet and MPLS-TP
Then I present a direct technical comparison of
Ethernet vs. MPLS-TP

## Slide 3: Access networks ?
CORE
MPLS or IP
interface
(and theoretically PBB)
ACCESS NETWORK
Q-in-Q ETHERNET ?
MPLS-TP ?
Internet
other customer sites
Data Centers
RESIDENTIAL CUSTOMERS
IP
BUSINESS CUSTOMERS
IP or Ethernet
CELL SITES
IP and/or ETHERNET
and/or TDM
and TIMING

## Slide 4: Why Ethernet and MPLS-TP ?
Ethernet started in the customer network (LAN) and for many years has moved into the access network (MEF)
MPLS started in the core network and is now trying to conquer the access network
customer network
ACCESS NETWORK
core
network
ETHERNET
MPLS
first mile
last mile

## Slide 5: Access network segmentation
A recent trend is to segment the access network into :
last/first mile
  provides connectivity from customer site to first access node
  leverages physical layer technologies such as :
  DSL, active/passive fiber, microwave, HSDPA+, LTE, …
middle mile
  collects and aggregates traffic from multiple access nodes
  provides backhaul towards core
Last / First Mile
Middle Mile
+
Access Node
NTU/CLE
Aggregation
Backhaul
ACCESS NETWORK

## Slide 6: access / core differences (1)
Differences between core networks and access networks
may translate into differences in protocol requirements
core has relatively few Network Elements (routers, LSRs, switches)
access has many NEs (CPEs, NTUs, DSLAMs, aggregators)
strong pressure on access NE price levels
access needs to be as touchless as possible
core runs higher data-rates
access runs lower data-rates (including DSL, PON, wireless)
core may guarantee QoS by resource overprovisioning
access requires QoS mechanisms

## Slide 7: access / core differences (2)
core is richly connected
access topology is simple (usually trees or rings)
fault in access network affects fewer customers
but fewer bypass options
core can get away with fast rerouting
access network requires OAM and planned APS
core NEs are well guarded
access NEs are easily accessible
core can be considered a walled garden from a security PoV
strong security to and from the outside world
loose security on the inside
customer networks too are usually considered walled gardens
but it is impractical to protect the entire access network

## Slide 8: Ethernet / MPLS-TP differences (1)
both Ethernet and MPLS-TP can transport IP and other clients
both Ethernet and MPLS-TP can transported over SDH and OTN
but there are fundamental protocol differences :
Ethernet defines a physical (L1) layers (but may run over MPLS)
MPLS requires a server layer to transport it (which may be Ethernet)
Ethernet frames are inherently self-describing
MPLS packets do not contain a Protocol ID
every Ethernet frame contains a
global non-aggregatable destination address
MPLS labels are only meaningful locally
every Ethernet frame contains a unique Source Address
MPLS packets contain no source identifier

## Slide 9: Ethernet / MPLS-TP differences (2)
both Ethernet and MPLS-TP define FM/PM OAM and APS
Ethernet does not define a routing protocol (neglecting TRILL, etc.)
but defines a number of L2 Control Protocols (L2CPs)
MPLS leverages the entire IP suite of protocols
Ethernet does not tolerate forwarding loops
MPLS can, since it contains a TTL field
Ethernet and MPLS both define 3-bit priority (DiffServ) marking
S-tagged Ethernet also supports Drop Eligibility marking
Carrier grade Ethernet supports bandwidth profiles (bucketing)
Ethernet defines timing (1588) and security (MACsec, 1X) protocols
A single entity claims to hold the pen
for both Ethernet (IEEE) and MPLS (IETF)
but in practice multiple competing SDOs engage in development

## Slide 10: Face - off
We can now compare Ethernet and MPLS-TP for access networks
We will consider the following criteria :
Fault Management functionality
Performance Management functionality
Automatic Protection Switching mechanisms
Quality of Service mechanisms
Traffic - handling diverse client types
Timing – high accuracy time and frequency distribution
Integration with surrounding networks
CAPEX
OPEX
Security
Each will be scored for :
suitability 2 points
coverage 4 points
maturity 4 points
WARNING :
these weightings are arbitrary
and may need adjustment for specific scenarios

## Slide 11: FM – the arguments
Access networks require strong Fault Management capabilities in order to minimize down-time
Ethernet, once without OAM now has two (Y.1731/CFM and EFM)
Having a unique source address
Ethernet is particularly amenable to trace-back functionality
QinQ is not true client-server, but this is covered up by Y.1731’s MEL
Y.1731 is full-featured – comprehensive set of FM TLVs
EFM is more limited, but adds dying gasp critical for CPEs
Interop issues of both OAMs have finally been resolved
and implementation agreements (e.g. MEF-30) resolve details
MPLS had no true full-featured OAM but had basic heartbeats (BFD) and diagnostics (LSP-ping)
The IETF designed MPLS-TP FM based on the GACh and
BFD for Continuity Check and Connectivity Verification
LSP-ping for on-demand diagnostics
new frame formats for other needs

## Slide 12: FM – the verdict
Suitability
Ethernet, having a Source Address, is highly suitable
MPLS, having no true addresses, requires extra work
BOTTOM LINE - Ethernet is more suitable (2 points 1 points)
Coverage
Y.1731 is full featured, EFM fulfills its requirements
MPLS-TP FM was designed to be similar to CFM
but is missing dying gasp
BOTTOM LINE – almost tie (4 points 3 points)
Maturity
Y.1731 and EFM are interoperable and widely deployed
some MPLS-TP features are now seeing initial trials
BOTTOM LINE - Ethernet wins a wide margin (4 points 1 point)
TOTAL 10 points 5 points

## Slide 13: PM – the arguments
Performance Management is a useful tool for
maintenance and diagnostics of the access network
The ITU Y.1731, but not the IEEE 802.1ag version
supports PM (loss, delay, PDV, …)
using a request-response model
Y.1731 is used as the base for commissioning procedures (Y.1564)
Widespread vendor interoperability has been demonstrated
RFCs 6374 and 6375 define a set of PM functions
based on the GACh
These functions were designed to be HW friendly, yet flexible
support byte or packet counters
1588 or NTP style timestamps
traffic-counters or synthetic loss
Implementations have yet to be announced

## Slide 14: PM – the verdict
Suitability
neither protocol has an inherent advantage or disadvantage
BOTTOM LINE – tie (2 points 2 points)
Coverage
both protocols support all features
MPLS may be more flexible
BOTTOM LINE - tie by design (4 points 4 points)
Maturity
Y.1731 is finally interoperable
MPLS PM is not yet (widely) implemented
BOTTOM LINE - Ethernet wins a wide margin (4 points 0 points)
TOTAL 10 points 6 points

## Slide 15: APS – the arguments
Automatic Protection Switching is a complex subject
and requires careful protocol work and proper configuration
In general we need solutions for both
linear (i.e., general topology) protection and
ring protection
Ethernet has a particular problem with rings
There are many open loop ring protection (e.g., G.8032)
but these are not compatible with QoS mechanisms
MPLS in the core exploits Fast ReRoute (RFC 4090) instead of APS
but FRR requires rich interconnection
and so is not usually applicable to access networks
The IETF has standardized RFC 6378 for MPLS-TP linear protection
and there are proposals for ring protection

## Slide 16: APS– the verdict
Suitability
Ethernet is not inherently suitable for ring protection
MPLS, has no particular strengths or weaknesses
BOTTOM LINE – MPLS easily wins (0 points 2 points)
Coverage
G.8031/G.8032 fulfill current requirements
RFC 6378 for linear protection, no ring protection RFC yet
BOTTOM LINE – Ethernet narrowly wins (3 points 2 points)
Maturity
G.8031/G.8032 have been extensively debugged
and have been updated more than once (is that good or bad?)
MPLS-TP APS is only partially finalized and not yet deployed
BOTTOM LINE - Ethernet wins (4 points 1 points)
TOTAL 7 points 5 points

## Slide 17: QoS – the arguments
Two types of QoS need to be considered
hard QoS (IntServ, Traffic Engineering)
Connection Admission Control and Resource Reservation
soft QoS (DiffServ, traffic conditioning)
priority marking, discard eligibility, queuing, bucketing algorithms
PBB-TE (PBT) defines hard QoS, but is not widely implemented
Ethernet has P-bits (PCP field) for prioritization marking
and S-tagged Ethernet has discard eligibility (DEI) marking
MEF’s BW profile defines a token bucketing algorithm
Ethernet headers are self-describing, and thus facilitating Traffic Awareness
MPLS-TE supports resource reservation but TE may not be relevant for access networks
MPLS Traffic Class (and L-LSPs) enable support for DiffServ prioritization
MPLS packets are not self-describing, requiring DPI for Traffic Awareness

## Slide 18: QoS – the verdict
Suitability
Ethernet supports all QoS types
MPLS does not define for (bucket-based) traffic conditioning
BOTTOM LINE – Ethernet narrowly wins (2 points 1 point)
Coverage
MEF standards have been field proven
w/o bucketing MPLS is at a disadvantage
BOTTOM LINE – Ethernet narrowly wins (4 points 3 points)
Maturity
Ethernet BW profiles are standardized
and there are recognized certification programs
MPLS-TP – nothing special
BOTTOM LINE - Ethernet wins a wide margin (4 points 0 points)
TOTAL 10 points 4 points

## Slide 19: Traffic – the arguments
No transport protocol is useful
if it can not transport the required client traffic
Ethernet carries traffic types via Ethertype marking or LLC
and can directly carry IPv4, IPv6, MPLS, Ethernet,
fiber channel, and low-rate TDM (MEF-8)
Ethernet does not directly carry other legacy traffic types
(e.g., ATM, frame relay)
but can indirectly carry them via PHP’ed MPLS PWs
MPLS can carry IPv4, IPv6, MPLS, and PWs
and PWs carry Ethernet, Fiber Channel and all legacy types
Defining a new PW type requires IETF consensus
but the new packet-PW provides more freedom!
Neither is universal
but existing mechanisms can be extended to cover new cases

## Slide 20: Traffic – the verdict
Suitability
Ethernet supports arbitrary clients via Ethertypes
MPLS supports arbitrary clients via PWs
BOTTOM LINE – tie (2 points 2 points)
Coverage
Ethernet does not support all legacy traffic types (ATM, FR)
MPLS, via PWs, supports most traffic types
BOTTOM LINE – MPLS wins (2 points 3 points)
Maturity
both Ethertypes and PWs are very widely deployed
BOTTOM LINE – tie (4 points 4 points)
TOTAL 8 points 9 points

## Slide 21: Timing – the arguments
Distribution of highly accurate timing
(both frequency and Time of Day)
is crucial for some access network applications (notably cellular backhaul)
Two protocols have become standard for this purpose
Synchronous Ethernet (SyncE) is Ethernet-specific (MPLS does not define a physical layer)
IEEE 1588-2008 (AKA 1588v2, presently defined for Ethernet and UDP/IP) for Timing over Packet on-path support elements (Boundary Clocks or Transparent Clocks)
have been defined for Ethernet
The IETF TICTOC WG is presently working on 1588oMPLS
but no MPLS-based timing protocols yet exist

## Slide 22: Timing – the verdict
Suitability
Ethernet supports ToP and defines a physical layer to support SyncE
MPLS may be able to support 1588 (but there will never be a SyncMPLS)
BOTTOM LINE – Ethernet wins (2 points 1 point)
Coverage
Ethernet meets all requirements with SyncE, 1588, BC, TC
1588oMPLS to support ToP is being proposed
BOTTOM LINE – Ethernet wins (4 points 1 point)
Maturity
ITU-T has defined profile(s) for 1588 use
MPLS presently has no timing support
BOTTOM LINE - Ethernet wins a wide margin (4 points 0 points)
TOTAL 10 points 2 points

## Slide 23: Integration – the arguments
The access network needs to integrate with
the core network
the customer network
Cost and complexity will be minimized by smooth hand-off
i.e., access protocol compatibility with other network protocol
Customer networks may have Ethernet or TDM interfaces
(IP over Ethernet, Ethernet over TDM, Ethernet over SDH)
So Ethernet in the access is a perfect match
MPLS is a reasonable match
since these protocols can be tunneled over MPLS
Core networks are usually MPLS (IP over MPLS, MPLS over Ethernet, MPLS over SDH)
MPLS-TP reuses existing MPLS standards
thus maximizing compatibility (stitching ? seamless ?)
Ethernet can not seamlessly interface with an MPLS core

## Slide 24: Integration – the verdict
Suitability
Ethernet is a perfect match for customer network, but not for core
MPLS-TP is the best match for core network, but not for customer
BOTTOM LINE – tie (1 point 1 point)
Coverage
Ethernet QinQ and MACinMAC perfect customer hand-off
MPLS-TP does not require a gateway for forwarding to core
but control protocols may not interconnect
BOTTOM LINE – neither is perfect (3 points 2 points)
Maturity
Ethernet QinQ is presently widely deployed
seamless MPLS is still in its infancy
BOTTOM LINE - Ethernet wins a wide margin (4 points 1 point)
TOTAL 8 points 4 points

## Slide 25: CAPEX – the arguments
Access network providers need to keep their costs down
Due to the large number of NEs
access networks are CAPEX sensitive
Ethernet switching fabrics are inherently nonscalable since its long global addresses can’t be aggregated
Due to popularity Ethernet switches are inexpensive
(high volumes, large R&D investment in cost reduction)
However, carrier-grade Ethernet switches need extra functionality
Ethernet supports CAPEX-saving architectures (e.g., EPON)
LSRs are complex and expensive
Reducing the price of NEs (MPLS switch instead of MPLS router)
was the (unstated) motivation for MPLS-TP
Pure MPLS NEs have simple forwarding engines
and thus should be less expensive than Ethernet switches but still require Ethernet or SDH or OTN interfaces

## Slide 26: CAPEX – the verdict
Suitability
Ethernet is inexpensive, but can not scale forever
MPLS-TP allows for significant cost reduction vs. full LSR (but vs. Eth ?)
BOTTOM LINE – MPLS wins (1 point 2 points)
Coverage
R&D and volumes have driven down Ethernet CAPEX
MPLS-TP-specific devices can be low cost
BOTTOM LINE – tie (4 points 4 points)
Maturity
MEF certification programs for carrier-grade Ethernet switches
Many trials are using (down-graded?) full LSRs
optimized chip sets are starting to emerge
BOTTOM LINE – advantage to Ethernet (4 points 2 points)
TOTAL 9 points 8 points

## Slide 27: OPEX – the arguments
OPEX considerations that we will take into account :
direct operations cost
staffing
minimizing unchargeable overhead
Reduction of direct operations costs
for networks with large number of NEs requires :
equipment to work reliably and interoperate
minimal touch (autodiscovery, zero-touch configuration, etc.)
use of FM, Control Plane or Management Plane protocols
Maintaining competent staff requires :
finding (need to be available)
training
retaining
Overhead minimization applies to :
per packet overhead
OAM, CP/MP packets

## Slide 28: OPEX – the arguments (cont.)
Basic Ethernet is zero-touch by design but carrier-grade features may add many configuration parameters
Ethernet has a large number of useful L2CPs (STP, ELMI, GVRP) but no universal CP protocol
In addition to equipment certification MEF has initiate certification for carrier Ethernet engineers
Main Ethernet overhead is large, but tags add only a small delta
Basic MPLS relies on IP routing protocols
but TP is designed to be able to function w/o a CP
GMPLS CP has been defined as an option
TP can operate without IP forwarding (eliminating IP logistics)
CP and MP can be carried in GACh (although not yet developed)
Specific vendors have expert certifications for MPLS
but none specific to MPLS-TP
TP is similar to other transport networks (look and feel)
in an effort to minimize retraining and may leverage extensions to existing OSS

## Slide 29: OPEX – the verdict
Suitability
Metro Ethernets have been shown to be low OPEX
MPLS-TP is designed to be inexpensively maintainable
BOTTOM LINE – tie (2 points 2 points)
Coverage
Ethernet has (inelegant) CP, available staff, medium overhead
MPLS-TP learned from previous efforts
BOTTOM LINE – tie (4 points 4 points)
Maturity
extensive experience and certification programs
extensive MPLS operational experience only partially applicable
BOTTOM LINE – Ethernet wins (4 points 2 points)
TOTAL 10 points 8 points

## Slide 30: Security – the arguments
Security is perhaps the most important telecomm issue today
OAM, APS, QoS mechanisms
are powerless to cope with Denial of Service attacks !
Access network NEs are frequently physically unprotected, so
ports must be protected
packets must be authenticated and integrity checked
confidentiality mechanisms may be needed
MPs and CPs must be hard-state
Ethernet packets carry unique authenticatable source addresses
MACsec and its 802.1X extensions define mechanisms
that can be used to protect carrier networks
(although the hop-by-hop security model may not always be ideal)
MPLS was designed for core networks (walled gardens)
with the assumption that there are no inside attacks
Forwarding plane can be attacked due to lack of authentication/integrity
Control plane can be attacked due to soft state protocols

## Slide 31: Security – the verdict
Suitability
Ethernet, has an authenticatable unique SA
MPLS has no source identifier and uses soft-state CPs
BOTTOM LINE – Ethernet wins by far (2 points 0 points)
Coverage
Ethernet has MACsec and 802.1X, but may need more
MPLS-TP has little positive support (but it does support attacks …)
BOTTOM LINE – Ethernet easily wins (3 points 1 point)
Maturity
MACsec is starting to appear in standard chipsets
MPLS community is completely ignoring the TP security problem
BOTTOM LINE - Ethernet clearly wins (2 points 0 points)
TOTAL 7 points 1 point

## Slide 32: The totals
The final scores :
Caveats :
Deployments have particular (non)requirements
but we gave equal weight to all 10 considerations
Some coverage and all maturity scores will change over time
Note: MPLS-TP lost
  8 points due to lack of timing support
  9 points due to lack of security
  and
  21 points due to lack of maturity on other subjects !
 | suitability | coverage | maturity | total
Ethernet | 16/20 | 35/40 | 38/40 | 89
MPLS-TP | 14/20 | 27/40 | 11/40 | 52

## Slide 33
Follow us at
raddata.blogspot.com