## Slide 1: the science behind FLASH
Yaakov (J) Stein

## Slide 2: Types of Memory
By memory we mean any device that stores bits of information
Volatile memory
requires voltage (and perhaps refresh) to maintained information
most frequently used for RAM
can be implemented by capacitors, flip-flops
Nonvolatile memory
can maintain memory for long periods of time without voltage
most frequently used for ROM, long-term storage
originally implemented by holes in paper, magnetic media, etc.
since the invention of integrated circuits can be implemented using solid-state devices such as PROM, EPROM, EEPROM and FLASH

## Slide 3: Simplest solid-state ROM
The simplest non-volatile solid state memory is the hard-coded (masked) ROM
To store the 4 nibbles 0101, 0110, 1100, 1011 we build the following matrix :
To retrieve the first (nth) nibble
place a voltage on the top (nth from top) word line and observe the bit lines
word lines
bit lines
Notes: In 1965 Sylvania produced a 256-bit bipolar TTL ROM for Honeywell that was programmed one bit at a time by a technician who physically scratched connections.
Later that year General Microelectronics produced a 1024-bit ROM (which was 4 times slower)

## Slide 4: Simplest solid-state ROM (cont.)
It is implemented purely with conductors
making it small and inexpensive
It must be programmed when the memory chip is fabricated
and can never be erased or reprogrammed
This severely limits its use
To improve on the hard-coded ROM
we will need to understand some solid-state physics

## Slide 5: Solid State Physics

## Slide 6: Solid State Physics
Solid state physics was mostly developed in Bell Labs
in order to enable new electronic devices
such as the diode RF detector and the transistor amplifier
SS physics explains why electrical resistivity varies over 32 orders of magnitude
superconductor 0 ohm-cm
metal at low temperature 10-10 ohm-cm
semiconductors 10-5 to 105 ohm-cm
good insulator 1022 ohm-cm
SS physics can only be understood through quantum mechanics
but we can grasp the main features by learning only a few facts

## Slide 7: Atomic shell model
Quantum mechanics teaches us that :
atoms are composed of nuclei surrounded by electrons
electrons occupy discrete states |n l m s > where
  n = 1, 2, 3, ... major shell number
  l = 0, 1, ..., n-1 electron’s angular momentum
  s (l=0), p (l=1), d (l=2), f (l=3), ...
  m = -l, ... l angular momentum projection
  s = ± ½ is the electron’s spin
no 2 electrons can occupy the same state
so with a given n, there can only be
2 s electrons, 6 p electrons, 10, d electrons, etc.
electrons in closed shells are tightly bound to the nucleus
electrons in open shells (valence electrons) can easily escape
1
2
3
4

## Slide 8: Periodic table
1 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 He
1s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1s2
3 Li | 4 Be |  |  |  |  |  |  |  |  |  |  | 5 B | 8 C | 7 N | 8 O | 9 F | 10 Ne
2s | 2s2 |  |  |  |  |  |  |  |  |  |  | 2s22p | 2s22p2 | 2s22p3 | 2s22p4 | 2s22p5 | 2s22p6
11 Na | 12 Mg |  |  |  |  |  |  |  |  |  |  | 13 Al | 14 Si | 15 P | 16 S | 17 Cl | 18 Ar
3s | 3s2 |  |  |  |  |  |  |  |  |  |  | 3s23p | 3s23p2 | 3s23p3 | 3s23p4 | 3s23p5 | 3s23p6
19 K | 20 Ca | 21 Sc | 22 Ti | 23 V | 24 Cr | 25 Mn | 26 Fe | 27 Co | 28 Ni | 29 Cu | 30 Zn | 31 Ga | 32 Ge | 33 As | 34 Se | 35 Br | 36 Kr
4s | 4s2 | 3d4s2 | 3d24s2 | 3d34s2 | 3d54s | 3d54s2 | 3d64s2 | 3d74s2 | 3d84s2 | 3d104s | 3d104s2 | 4s24p | 4s24p2 | 4s24p3 | 4s24p4 | 4s24p5 | 4s24p6
37 Rb | 38 Sr | 39 Y | 40 Zr | 41 Nb | 42 Mo | 43 Tc | 44 Ru | 45 Rh | 46 Pd | 47 Ag | 48 Cd | 49 In | 50 Sn | 51 Sb | 52 Te | 53 I | 54 Xe
5s | 5s2 | 4d5s2 | 4d25s2 | 4d45s | 4d55s | 4d65s | 4d75s | 4d85s | 4d10 | 4d105s | 4d105s2 | 5s25p | 5s25p2 | 5s25p3 | 5s25p4 | 5s25p5 | 5s25p6
55 Ce | 56 Ba | 57 La | 72 Hf | 73 Ta | 74 W | 75 Re | 76 Os | 77 Ir | 78 Pt | 79 Au | 80 Hg | 81 Tl | 82 Pb | 83 Bi | 84 Po | 85 At | 86 Rn
6s | 6s2 | 5d6s2 | 4f143d24s2 | 5d36s2 | 5d46s2 | 5d56s2 | 5d66s2 | 5d9 | 5d96s | 5d106s | 5d106s2 | 6s26p | 6s26p2 | 6s26p3 | 6s26p4 | 6s26p5 | 6s26p6
The shell model explains the periodic table
periods (rows) correspond to the value of n (right column is full shell)
groups (columns) correspond to the number of electrons in the open shell
elements in the same group have similar chemical properties
Leftmost group has 1 electron in outer shell (“valence” electron)
Rightmost group has fully closed shells – inert gases

## Slide 9: Noble Metals
 | 1 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 He | 
 | 1s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1s2 | 
 | 3 Li | 4 Be |  |  |  |  |  |  |  |  |  |  | 5 B | 8 C | 7 N | 8 O | 9 F | 10 Ne | 
 | 2s | 2s2 |  |  |  |  |  |  |  |  |  |  | 2s22p | 2s22p2 | 2s22p3 | 2s22p4 | 2s22p5 | 2s22p6 | 
 | 11 Na | 12 Mg |  |  |  |  |  |  |  |  |  |  | 13 Al | 14 Si | 15 P | 16 S | 17 Cl | 18 Ar | 
 | 3s | 3s2 |  |  |  |  |  |  |  |  |  |  | 3s23p | 3s23p2 | 3s23p3 | 3s23p4 | 3s23p5 | 3s23p6 | 
 | 19 K | 20 Ca | 21 Sc | 22 Ti | 23 V | 24 Cr | 25 Mn | 26 Fe | 27 Co | 28 Ni | 29 Cu | 30 Zn | 31 Ga | 32 Ge | 33 As | 34 Se | 35 Br | 36 Kr | 
 | 4s | 4s2 | 3d4s2 | 3d24s2 | 3d34s2 | 3d54s | 3d54s2 | 3d64s2 | 3d74s2 | 3d84s2 | 3d104s | 3d104s2 | 4s24p | 4s24p2 | 4s24p3 | 4s24p4 | 4s24p5 | 4s24p6 | 
 | 37 Rb | 38 Sr | 39 Y | 40 Zr | 41 Nb | 42 Mo | 43 Tc | 44 Ru | 45 Rh | 46 Pd | 47 Ag | 48 Cd | 49 In | 50 Sn | 51 Sb | 52 Te | 53 I | 54 Xe | 
 | 5s | 5s2 | 4d5s2 | 4d25s2 | 4d45s | 4d55s | 4d65s | 4d75s | 4d85s | 4d10 | 4d105s | 4d105s2 | 5s25p | 5s25p2 | 5s25p3 | 5s25p4 | 5s25p5 | 5s25p6 | 
 | 55 Ce | 56 Ba | 57 La | 72 Hf | 73 Ta | 74 W | 75 Re | 76 Os | 77 Ir | 78 Pt | 79 Au | 80 Hg | 81 Tl | 82 Pb | 83 Bi | 84 Po | 85 At | 86 Rn | 
 | 6s | 6s2 | 5d6s2 | 4f143d24s2 | 5d36s2 | 5d46s2 | 5d56s2 | 5d66s2 | 5d9 | 5d96s | 5d106s | 5d106s2 | 6s26p | 6s26p2 | 6s26p3 | 6s26p4 | 6s26p5 | 6s26p6 | 
Copper, silver, and gold have one valence electron
The closed shell ions form a close-packed crystalline structure
and the extra electrons are “free electrons” shared by all atoms
These free electrons contribute to electric and thermal conductivity, and luster
10
1 valence
electron

## Slide 10: The semiconductors
 | 1 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 He | 
 | 1s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1s2 | 
 | 3 Li | 4 Be |  |  |  |  |  |  |  |  |  |  | 5 B | 8 C | 7 N | 8 O | 9 F | 10 Ne | 
 | 2s | 2s2 |  |  |  |  |  |  |  |  |  |  | 2s22p | 2s22p2 | 2s22p3 | 2s22p4 | 2s22p5 | 2s22p6 | 
 | 11 Na | 12 Mg |  |  |  |  |  |  |  |  |  |  | 13 Al | 14 Si | 15 P | 16 S | 17 Cl | 18 Ar | 
 | 3s | 3s2 |  |  |  |  |  |  |  |  |  |  | 3s23p | 3s23p2 | 3s23p3 | 3s23p4 | 3s23p5 | 3s23p6 | 
 | 19 K | 20 Ca | 21 Sc | 22 Ti | 23 V | 24 Cr | 25 Mn | 26 Fe | 27 Co | 28 Ni | 29 Cu | 30 Zn | 31 Ga | 32 Ge | 33 As | 34 Se | 35 Br | 36 Kr | 
 | 4s | 4s2 | 3d4s2 | 3d24s2 | 3d34s2 | 3d54s | 3d54s2 | 3d64s2 | 3d74s2 | 3d84s2 | 3d104s | 3d104s2 | 4s24p | 4s24p2 | 4s24p3 | 4s24p4 | 4s24p5 | 4s24p6 | 
 | 37 Rb | 38 Sr | 39 Y | 40 Zr | 41 Nb | 42 Mo | 43 Tc | 44 Ru | 45 Rh | 46 Pd | 47 Ag | 48 Cd | 49 In | 50 Sn | 51 Sb | 52 Te | 53 I | 54 Xe | 
 | 5s | 5s2 | 4d5s2 | 4d25s2 | 4d45s | 4d55s | 4d65s | 4d75s | 4d85s | 4d10 | 4d105s | 4d105s2 | 5s25p | 5s25p2 | 5s25p3 | 5s25p4 | 5s25p5 | 5s25p6 | 
 | 55 Ce | 56 Ba | 57 La | 72 Hf | 73 Ta | 74 W | 75 Re | 76 Os | 77 Ir | 78 Pt | 79 Au | 80 Hg | 81 Tl | 82 Pb | 83 Bi | 84 Po | 85 At | 86 Rn | 
 | 6s | 6s2 | 5d6s2 | 4f143d24s2 | 5d36s2 | 5d46s2 | 5d56s2 | 5d66s2 | 5d9 | 5d96s | 5d106s | 5d106s2 | 6s26p | 6s26p2 | 6s26p3 | 6s26p4 | 6s26p5 | 6s26p6 | 
4
4
C, Si and Ge have 4 valence electrons and 4 vacancies in the outer shell
In diamond structure each atom can form a covalent bond with 4 nearest neighbors
This enables sophisticated chemistry
Carbon – biology
Silicon – geology
Silicon and Germanium – solid state electronics

## Slide 11: Compound Semiconductors
We can also make semiconductors from
an atom with 3 free electrons and 5 vacancies (e.g., Al, Ga, In)
an atom with 5 free electrons and 3 vacancies (e.g., P, As, Sb)
Thus InSb, InAs, InP, GaP, GaAs, GaSb, AlP, AlAs, AlSb
are also semiconductors
and are used in solid-state devices
1 H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 He
1s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1s2
3 Li | 4 Be |  |  |  |  |  |  |  |  |  |  | 5 B | 8 C | 7 N | 8 O | 9 F | 10 Ne
2s | 2s2 |  |  |  |  |  |  |  |  |  |  | 2s22p | 2s22p2 | 2s22p3 | 2s22p4 | 2s22p5 | 2s22p6
11 Na | 12 Mg |  |  |  |  |  |  |  |  |  |  | 13 Al | 14 Si | 15 P | 16 S | 17 Cl | 18 Ar
3s | 3s2 |  |  |  |  |  |  |  |  |  |  | 3s23p | 3s23p2 | 3s23p3 | 3s23p4 | 3s23p5 | 3s23p6
19 K | 20 Ca | 21 Sc | 22 Ti | 23 V | 24 Cr | 25 Mn | 26 Fe | 27 Co | 28 Ni | 29 Cu | 30 Zn | 31 Ga | 32 Ge | 33 As | 34 Se | 35 Br | 36 Kr
4s | 4s2 | 3d4s2 | 3d24s2 | 3d34s2 | 3d54s | 3d54s2 | 3d64s2 | 3d74s2 | 3d84s2 | 3d104s | 3d104s2 | 4s24p | 4s24p2 | 4s24p3 | 4s24p4 | 4s24p5 | 4s24p6
37 Rb | 38 Sr | 39 Y | 40 Zr | 41 Nb | 42 Mo | 43 Tc | 44 Ru | 45 Rh | 46 Pd | 47 Ag | 48 Cd | 49 In | 50 Sn | 51 Sb | 52 Te | 53 I | 54 Xe
5s | 5s2 | 4d5s2 | 4d25s2 | 4d45s | 4d55s | 4d65s | 4d75s | 4d85s | 4d10 | 4d105s | 4d105s2 | 5s25p | 5s25p2 | 5s25p3 | 5s25p4 | 5s25p5 | 5s25p6
55 Ce | 56 Ba | 57 La | 72 Hf | 73 Ta | 74 W | 75 Re | 76 Os | 77 Ir | 78 Pt | 79 Au | 80 Hg | 81 Tl | 82 Pb | 83 Bi | 84 Po | 85 At | 86 Rn
6s | 6s2 | 5d6s2 | 4f143d24s2 | 5d36s2 | 5d46s2 | 5d56s2 | 5d66s2 | 5d9 | 5d96s | 5d106s | 5d106s2 | 6s26p | 6s26p2 | 6s26p3 | 6s26p4 | 6s26p5 | 6s26p6

## Slide 12: Semiconductor conductivity
At low temperatures a pure semiconductor is an insulator
What can make a semiconductor conduct electricity ?
increasing temperature
random energy breaks covalent bonds freeing electrons
(note that increasing temperature increases resistance of a conductor!)
doping (adding impurities)
N-type : replace a small percentage of atoms with valence 5 (P, As, Sb) donor atoms
P-type : replace a small percentage of atoms with valence 3 (B, Al, Ga) acceptor atoms
this introduces a small number of free electrons (or holes)
Note: doping usually replaces fewer than 1 in 10,000 atoms
field effect
applying a field to bring in free electrons from somewhere else

## Slide 13: Julius Lilienfeld
Julius Edgar Lilienfeld was a Jewish scientist at the University of Leipzig
Among his inventions are
the Field Effect Transistor (US patent 1745175)
the electrolytic capacitor
Xray tubes for medical uses
He moved to the United States in 1927 to better defend his patents
When Bardeen, Brattain, and Shockley (Bell Labs) produced the first working transistor in 1947 their patent applications were rejected due to Lilienfeld’s patents
Lilienfeld’s early work was on motion of electrons in vacuum
but the breakthrough came when he started observing their motion in solids
Notes: Lilienfeld has been mostly forgotten, never received Nobel for his discoveries

## Slide 14: Field Effect
When you place an electric field on a
insulator the field penetrates the insulator
but/because there are no free charges to move
conductor the field is blocked
because the free electrons move to block the field
semiconductor the field penetrates somewhat into the solid
free charges move around
If we put a voltage on this device
making GATE positive with respect to BODY
electrons will flow towards GATE
but will stop there because of the insulator
Now the semiconductor has free electrons
and current can flow between SOURCE and DRAIN
Conductor
Insulator
Semiconductor
GATE
BODY
SOURCE
DRAIN
pad

## Slide 15: MOSFET
This is the idea behind the Metal-Oxide-Semiconductor Field Effect Transistor
In practice
the Metal may be any conductor (and today is often non-metallic polysilicon)
the Oxide any insulator (today most often SiO2)
the body is often connected to the source (making the device unidirectional)
Compared to junction transistors
source ↔ emitter
gate ↔ base
drain ↔ collector
Metal
Oxide
Semiconductor
GATE
SOURCE
DRAIN
N
N
P
Notes: Instead of metal, most MOSFETs today use polysilicon (polycrystalline silicon).
The Oxide can be any high k dielectric.
We describe an “enhancement mode” NMOS MOSFET
where the source and drain are N+ semiconductors, and the channel is P type.
In PMOS the source and drain are P+ and the channel is N.

## Slide 16: MOSFET as an amplifier
When no voltage is applied to the gate
no current flows from source to drain
When a low voltage is applied to the gate
a narrow conduction channel is formed
allowing a small amount of current to flow
When a high voltage is applied to the gate
a wide conduction channel is formed
allowing a large amount of current to flow
So, the MOSFET can be used as an amplifier
GATE
SOURCE
DRAIN
GATE
SOURCE
DRAIN

## Slide 17: MOSFET as a switch
By either applying either zero or a large positive voltage
the MOSFET can be used as a switch
When no voltage on the gate the switch is OFF
no conductivity between source and drain
When sufficient voltage on the gate the switch is ON
conductivity between source and drain
The MOSFET is now the main component of digital electronics !
0 v
1 v
OFF
0 v
ON
1 v
1 v
1 v

## Slide 18: MOSFET History
1925 Julius Edgar Lilienfeld invents FET and patents the idea US 1745175
1947 Bardeen, Brattain, and Shockley (Bell Labs) build first working transistor
bipolar junction transistor based on 2 P-N junctions (PNP or NPN)
awarded 1956 Nobel Prize in Physics
1960 Dawon Kahng and Martin Atalla (Bell Labs) invent MOSFET
Although the bipolar transistor was once more popular
the MOSFET is now by far the most prevalent transistor
This is for 2 reasons
because the GATE is separated from the SOURCE by an insulator
the MOSFET’s input impedance is very high (unlike the bipolar transistor)
2. because it is easy to form SiO2 on Silicon (by heating in the presence of Oxygen)
MOSFETs are very inexpensive to produce
Notes: Kahng (Korean-American) also co-invents the FG MOSFET, after retiring founding president of the NEC Research Institute in NJ
Atalla (Egyptian from Port Said) who was Kahng’s boss, goes on to co-found HP Semiconductors and to invent the PIN number

## Slide 19: Floating Gate Memory Cell

## Slide 20: Floating Gate MOSFET
One day the lead to a MOSFET’s GATE broke off
and when trying to reconnect it a new device is invented
the Floating Gate MOSFET
The floating gate is completely surrounded by an insulator
(it itself may be a conductor)
So any electrons in the floating gate
are trapped there (will remain for many years!)
Above the FG is the control gate
When applying a positive voltage to the CG
electrons trapped in the FG
mask some of the field
So a higher voltage is needed for conductance
CONTROL GATE
SOURCE
DRAIN
FLOATING GATE
v
0
0.5
1
2
2.5
FET conducts with no electrons trapped in FG
FET conducts even with electrons trapped in FG
1.5
Notes: In Saifun’s “charge trap flash” the FG is an insulator
The voltages are typical but arbitrary, for demonstration only

## Slide 21: FG-MOSFET as a single-bit memory
Since the floating gate is surrounded by an insulator
trapped electrons can not escape
and will remain there for many years
Thus, a FG-MOSFET can be used as a non-volatile memory cell with one bit of memory
0 if the FG holds charge
1 if the FG has no charge
The element starts (uncharged) as 1
and must be written (charged) to contain 0
In order to actually utilize the FG-MOSFET, we need methods to
read the cell (find out if charge is trapped in the FG or not)
write the cell (inject charge into the FG, causing it to store a 0)
erase the cell (extract the charge from the FG, returning it to the default 1)
Notes: Dov Frohman says that Intel promised that EPROM memory would be maintained 10 years, but this was a wild guess!
It turned out to be true (even more than 10 years)

## Slide 22: Reading a FG MOSFET
To read the bit stored in the cell
apply 1 volt to gate
apply 1 volt to source
observe drain voltage
  if no charge on FG then transistor conducts, and 1v appears at drain
  if charge on FG then transistor does not conduct, and 0 voltage at drain
1 v
1 v
NO
CHARGE
1 v
1 v
1 v
WITH
CHARGE
0 v
v
0
0.5
1
2
2.5
FET conducts with no electrons trapped in FG
FET conducts even with electrons trapped in FG
1.5

## Slide 23: Writing (programming) a FG-MOSFET
The floating gate is completely insulated from the outside world
How do we insert and remove electrons in order to write/erase it ?
To write (program) a FG-MOSFET means to change it from its default 1 to 0
The most prevalent way of writing is hot carrier injection
The insulation around the floating gate is very thin (under 100 nm)
so high energy electrons can traverse it
To write via hot electron injection:
ground the source
  place a positive voltage on the gate
for a short period of time:
  place a very high positive voltage
  on the drain (to accelerate the electrons)
0 v
2 v
20 v
Notes: We will discuss later hot carrier degradation which causes wear, limiting the number of cycles it can endure
We discussed electrons as carriers, there can also be hole injection
injection times are typically 10s of milliseconds

## Slide 24: Erasing a FG-MOSFET
How do we erase a floating gate cell
(i.e., remove electrons from the insulated floating gate) ?
Hot electron injection is not possible (since we can’t energize trapped electrons!)
Two methods can be used :
ionize the insulator to make it conduct
quantum tunneling (Fowler-Nordheim tunneling)
Ionization means applying a strong field (e.g., by X-rays or ultraviolet light)
in order to rip electrons from their closed shells
These free electrons now conduct, and allow trapped electrons to escape
EPROMs have quartz windows to allow UV light in
Notes: Ralph Fowler (British) and Lothar Wolfgang Nordheim (German Jewish) physicists discovered that electron emission from surface of solids in electric field occurred because of tunneling, and wrote the basic equations to describe the phenomenon.

## Slide 25: Tunneling
One of the more surprising aspects of quantum physics is
the uncertainty theorem
The uncertainty theorem tells us
that an electron can not be completely localized
but rather has a spatial probability distribution
The distribution becomes wider
when the electron’s momentum is known better
Even when there is a barrier (such as an thin insulating slab)
an electron has finite probability
of appearing at the other side of the barrier
This purely quantum mechanics phenomenon is called tunneling
The probability of tunneling through a barrier
decreases exponentially with the barrier’s width
x
x

## Slide 26: Erasing a FG-MOSFET via tunneling
To erase a floating gate cell (return the bit to 1) via tunneling
ground the body
place a very high negative voltage pulse on the gate
drawing away electrons that have tunneled through the insulator
Equivalently
ground the gate
place a very high positive pulse on the body
It is also possible to write a floating gate cell (set bit to 0) via tunneling
by reversing the voltage pulse
attracting electrons that have tunneled though
-20 v
0 v
+20 v
0 v
Notes: Note that in many cases the body is connected to the source

## Slide 27: FG MOSFET Memory History
1967 Kahng and Simon Sze (Bell Labs) invent FG MOSFET
1971 Dov Frohman (Intel) invents EPROM without knowing about Kahng & Sze
awarded US patent 3660819, and produced 1702 2K EPROM
1977 Eli Harari (Hughes) invents EEPROM, awarded US patent 4,115,914
1978 George Perlegos (Intel) also invents EEPROM, awarded US patent 4,203,158
1980 Fujio Masuoka (Toshiba) invents NOR Flash, awarded US patent 4,531,203
1987 Fujio Masuoka (Toshiba) invents NAND Flash
1991 SanDisk announces 20 MB flash-based solid state drive (SSD)
1995 M-Systems announces flash-based HDD replacement drive
1999 USB flash drive invented by Amir Ban, Dov Moran, Oron Ogdon (M-Systems)
awarded US patent 6,148,354 and manufacture “DiskOnKey”
1999 USB flash drive also invented by Shimon Shmueli (IBM)
Notes: Dov worked with Intel founders Gordon Moore and Robert Noyce at Fairchild, remained at Fairchild while finishing PhD, followed them to Intel a year later
After inventing EPROM left Intel to teach in Ghana, returned to Intel and convinced Moore to open Intel Israel
Intel was originally SRAM / DRAM memory chip vendor, went into microprocessors when Japanese took over that market
Eli Harari co-founds SanDisk in 1988
George Perlegos left Intel and founded Atmel

## Slide 28: Summary: Nonvolatile SS Memory
Type | Invented | Programming | Erasing
ROM | 1965 | masking (hard coded) | N.A.
PROM | 1967 Kahng & Sze (Bell Labs) | hot carrier injection | N.A.
EPROM | 1971 Dov Frohman (Intel) | hot carrier injection | ultraviolet ionization
EEPROM | 1978 Eli Harari (Hughes) George Perlegos (Intel) | tunneling | tunneling
FLASH (NOR/NAND) | 1980 / 1987 Fujio Masuoka (Toshiba) | hot carrier injection | tunneling

## Slide 29: Multilevel FG MOSFET
Up to now we have assumed that the floating gate was either charged or uncharged
But we can readily inject different amounts of charge
resulting in a FG-MOSFET with different voltage thresholds for conductance
0.5 v
0
CHARGE
v
0
0.5
1
2
2.5
1.5
1 v
1
CHARGE
1.5 v
2
CHARGE
2 v
3
CHARGE

## Slide 30: MLC
The multilevel FG-MOSFET can be used
as a non-volatile memory cell with more than 1 bit of memory
In this context we call our previous FG transistor a Single Level Cell (SLC)
and the multilevel FG transistor a Multi Level Cell (MLC)
Since MLC stores multiple bits in each cell (4 for 2 bits, 8 for 3 bits, 16 for 4 bits)
MLC has higher storage density than SLC
Since MLC requires more accurate charge amounts and gate voltages (low margin)
MLC has higher error probability than SLC, MLC degrades faster than SLC
MLC with additional mechanisms to improve reliability is called enterprise MLC (eMLC)
These mechanisms include
overprovisioning (manufacturing with more physical memory than advertised)
error correcting codes (additional bits for error corrections)
wear levelling (remapping physical memory blocks to equalize cell usage)
Notes: we will discuss the mechanism later

## Slide 31: Using MLC
To decode MLC
use Gray code, e.g., 11 10 00 01, to decrease BER
To read MLC
apply 1v to source
iteratively apply 0.75v, 1.25v, 1.75v, and 2.25v to gate
observe at which gate voltage drain voltage appears
To write MLC
apply multiple pulses for hot carrier injection
To update MLC (can increase charge without erasing)
apply additional pulses for hot carrier injection
To erase MLC
use tunneling as for SLC
v
0
0.5
1
2
2.5
1.5
Notes: With some MLC can apply one voltage and decode FG state based on current
Shuky Bruck has written articles on coding schemes for MLC (such as rank modulation, push-to-top)

## Slide 32: SLC or MLC
MLC provides more storage per chip size
and is thus much less expensive per bit
SLC is faster (no need for iteration)
SLC has lower intrinsic Bit Error Rate
SLC has longer life span
SLC can be manufactured for wider “industrial” temperature range
MLC is limited to “commercial” range since higher temperatures cause leakage
For these reasons
MLC is used for practically all consumer applications
SLC is used for enterprise applications

## Slide 33: Hot Carrier Degradation
Writing and erasing processes force electrons through the thin insulation layer
causing physical damage (e.g., damage traps)
Eventually the cell fails
Thus cells are rated with a maximum number of Program/Erase cycles (PE cycles)
The number of PE cycles depends on
the thickness of the insulation layer
the composition
the voltages used for hot carrier insertion
A raw FG cell may start to degrade after only 5,000 cycles, yet
commercial flash devices are typically guaranteed for 100,000 cycles
1 million cycle devices have been announced
there is research into self-healing memory with ratings of 100 million cycles
Notes: “raw” means without ECC and other mechanisms

## Slide 34: NOR and NAND Flash

## Slide 35: Fujio Masuoka
Fujio Masuoka developed Toshiba’s popular 1 Mb DRAM chip in the 1970s
In 1975 he conceived of nonvolatile flash memory
A colleague called it flash because erasing reminded him of a camera’s flash
Toshiba was not interested, so Masuoka worked on it on his own time
In 1980 received the key patents for NOR flash
In 1984 he presented flash
at the International Electronics Developers Meeting in San Francisco
Many US companies (including Intel) were interested and asked Toshiba for samples
Toshiba feared that flash would threaten its DRAM market
and did not produce a commercial product
Intel captured most of the flash chip market
In 1987 Masuoka invented the NAND flash
Notes: Masuoka received a promotion because of DRAM designs, and thus had subordinates, and so stated working on productization of flash
Toshiba forced Masuoka out, and he became a university professor instead
Invented NAND while being forced out of Toshiba
Intel left DRAM market because of Toshiba, but captured most of the flash market

## Slide 36: Memory arrays
Up to now we have discussed individual memory cells
In order to make memory chips, we can arrange these cells into rectangular arrays
Typically
a memory chip has thousands of blocks
data is erased in blocks
a block typically has 64 or 128 pages
data is written (and perhaps read) in pages
a page typically has 2K or 4K cells
a cell has 1, 2, or 3 bits
1 bit for SLC, >1 bit for MLC
A memory chip also needs addressing circuitry
in order to locate the required memory cell

## Slide 37: NOR and NAND Flash
There are 2 different interconnection topologies in wide use
NOR flash
NAND flash
The names come from the similarity with conventional NOR and NAND logic gates
In NOR flash, the bits of the drains of all words are ORed together
if one bit is 1 then the bit line is 1
In NAND flash, the bits of the drains of all words are ANDed together
if one bit is 0 then the bit line is 0
In both cases, the bit states are the opposites (negation) of the charge on the FG
the existence of trapped electrons represents a 0 bit
Notes: AND (negative of charge on FG) with (voltage on gate) to get drain voltage
no FG charge (1) and no gate voltage (0) results in no drain voltage (0)
FG charge (0) and no gate voltage (0) results in no drain voltage (0)
no FG charge (1) and gate voltage (1) results in drain voltage (1)
FG charge (0) and gate voltage (1) results in no drain voltage (0)

## Slide 38: NOR Flash Geometry
word lines
bit lines
Vs
Notes: in this toy example (fashioned after the first ROM example) we have 4-bit words, and 4 words in a page
note that the following are connected in parallel: all the sources in the page, all the gates in a word, all the nth bits in the page
explain bit line performs OR on all drains

## Slide 39: Reading NOR Flash
To read a word in SLC NOR flash memory
set Vs = 1 v (this is the normal state, only changed for write/erase operations)
this applies 1 v to the sources of all cells in the page
set the word line of the desired memory word to 1 v
this applies 1 v on the gates of all cells in the word
causing uncharged cells to conduct
observe the bit lines
For example, if the stored word is 0101, then we have the following
1 v
1 v
1 v
1 v
0 v
0 v
0
1
0
1
Notes: address circuitry is used to convert an address (16782) to a page and a word in the page, and this line is then asserted

## Slide 40: Writing and Erasing NOR Flash
Writing (charging the FG, setting the content to 0) is performed by hot charge injection
based on the procedure for the individual FG-MOSFET
set Vs = 0
place a positive voltage on the word line
place a very high positive voltage pulse on the bit lines to be written
Erasing (discharging the FG, setting the contents back to default 1) is via tunneling
based on the procedure for the individual FG-MOSFET
assuming the body is connected to the source
ground the word lines
place a very high positive voltage pulse on Vs
Notes: for erasing, we assume that the source is connected to the body

## Slide 41: NOR Flash Advantages and Disadvantages
The NOR design is conceptually simple
By intersecting a word line with a bit line, individual cells are accessible
With standard implementation, NOR memory enables random word-level access
NOR flash is used when random access is required
NOR is popular in mobile phones
But, the NOR design is very complex to build because of 3 separate lines to be routed
Vs
word lines
bit lines
Connecting the semiconductor to the conductor lines requires large metallic pads
about 60% of the chip area is pads and conductor lines
An alternative geometry called NAND flash addresses these issues

## Slide 42: NAND Flash Geometry
Vs
word lines
bit lines
Notes: in this toy example (fashioned after the other examples) we have 4-bit words, and 4 words in a page
note that the sources and drains are connected in series instead of in parallel
explain that bit is AND of all channel states
now how much smaller the area is, mostly because we don’t need pads, but also since we don’t need as many long conductor lines

## Slide 43: Reading NAND Flash
To read a word in SLC NAND flash memory
set Vs = 1 v (this is the normal state, only changed for write/erase operations)
this applies 1 v to the sources of all cells in the page
set the word line of the desired memory word to 1 v
this causes the uncharged ones to conduct
set the word line of all the other words to 2 v
this causes all cells to conduct
observe the bit lines
For example, if the stored word is 0101
the memory operation is depicted on the following slide

## Slide 44: NAND Flash example
1v
1v
2v
0
1
0
1
1 v
1 v
0 v
0 v

## Slide 45: NAND Chip Optimization
The NAND design is conceptually complex
but is much simpler to build than NOR flash
and does not require as many large pads to connect to metallic lines
NAND geometry intrinsically has the same capabilities as NOR geometry
by intersecting a word line with a bit line, individual cells are accessible
However, NAND area is much smaller for a given number of cells
conversely, the memory size is much larger for a given area
So chip designers optimize NAND flash chips even further
and limit the addressing circuitry to read full pages rather than individual words
This level of addressability is what is needed for SSDs
since HDDs are sector-addressable, not byte-addressable
MP3 players, digital cameras and USB drives also use NAND flash
Notes: HDD sectors are traditionally 512 bytes, but now 4K is more popular (e.g., Linux sector)

## Slide 46: NOR or NAND
NAND flash is more compact than NOR flash
NOR flash has read/write to individual words (can be used like DRAM)
NAND flash read/writes at the page level
NOR flash is faster than NAND at reading
although NAND speed is enough for consumer applications (even digital video)
NAND flash is faster at write and erase operations
NAND is thus better for general data storage and NOR for application program storage
NAND’s fast write/erase speed, higher density, and lower cost
make it the standard for most consumer applications
(USB drives, HDD replacement, MP3 players, smartphones, digital cameras)
NOR’s addressability, longer lifetime and faster read
favor it for data-center/enterprise applications, BIOS and on-chip memory

## Slide 47: Special Flash Mechanisms

## Slide 48: Making Flash Even Better
We have seen that flash suffers from several problems
bits can be incorrectly read
individual words can not be erased, only entire blocks
there is a limit to the number of PE cycles until a cell fails
Mechanisms have been designed to overcome these problems
Error Correcting Codes
Block Management
TRIM
Wear leveling
Read/Write Disturb handling
Garbage collection
Write amplification avoidance

## Slide 49: Error Correcting Codes
FG cells can be misread and can fail
BER of an unused SLC is about 10-8
after thousands of PE cycles it can be 10-6 (and MLC can reach over 10-4)
An error detection code determines (with high probability) whether we read correctly
An error correction code additionally supplies the correct bits (up to a limit)
Error detection/correction is built into the flash chip and adds overhead bits
typically each 2KB block will have an additional 64B of ECC overhead
ECC that can correct 4 bits out of 512B are in common use
01011001
01001010
00100000
01010011
01110100
01100101
01101001
01101110
0
1
1
0
0
0
0
1
01011001
01001010
00100000
01010011
01110100
01100101
01101001
01101110
0
1
1
0
0
0
0
1
01110110
parity-check error detection
2D parity-check error correction
Notes: explain that ECC theory is based on advanced algebra (Galois fields, etc)
Anobit (Herzeliya, acquired by Apple) has multiple patents on advanced ECC for flash (takes into account error statistics)

## Slide 50: Block Management
Flash chips are manufactured with more than the advertised capacity
this overprovisioning can be 7% for consumer grade and 30% for enterprise
A new flash chip may be shipped with failed blocks (to increase the yield) !
and additional blocks will fail over time (or removed from use based on PE cycles)
Overprovisioning extends the chip lifetime until there are too many failed blocks
Thus, we require a function to map the logical block to a physical one
and to perform maintenance and garbage collection
This function can be performed by the host in a device driver or Flash File System
or on-chip by a flash controller, or Flash Storage Processor
The FFS or FSP maintains
the free physical block pool
the bad (invalid) block list
the Physical Block Address to the Logical Block Address (used by OSs) lookup table
Notes: Commercial 120G drives actually have 128G, some chips even have 100% overprovisioning
Flash file systems : TrueFFS from M-Systems, JFFS2 from Microsoft, YAFFS, F2FS now in Linux kernel
In 1994 PCMCIA approved the Flash Translation Layer (FTL) specification, based on TrueFFS. Intel endorsed this spec.

## Slide 51: Bad Blocks
Bad blocks are blocks that can no longer be used
Bad blocks can be detected by
having been marked bad by the manufacturer
error detection upon read
bad status upon attempted erase (not all cells returned to 1 state)
not being able to completely write during a write attempt
Bad block management can be handled by the FSP, or device driver, or the file-system
Once there is an excessive number of bad blocks
the chip must be declared to have failed
Notes: not every read ECC error causes marking block bad

## Slide 52: TRIM
Deleting a file from a hard disk involves updating OS metadata (FAT, directory pointer)
the file data is not overwritten until needed
In order to free up space on a flash drive, blocks need to be actually erased
When SSDs started replacing HDDs in computer environments
the new TRIM command was added to the SATA disk interface
TRIM allows the OS to inform an SSD that a block is no longer in use
something meaningless for magnetic disks
Thus, rather than physically erasing the block in advance
the FSP merely marks the block for garbage collection

## Slide 53: Wear Leveling
10,000 PE cycles sounds like a lot
but if we cycle once a minute, this translates to a single week !
In many applications, certain blocks of data will be repeatedly rewritten
while others will remain untouched, or only read
Wear leveling prolongs the lifetime of a flash chip
by keeping track of the number of PE cycles for each block
and dynamically remapping blocks in order to equalize PE cycles
Thus, fewer blocks prematurely fail due to excessive PE cycles
Note: with TRIM only, released blocks are reused, but static blocks remain unused
With wear leveling, static blocks are periodically moved
spreading PE cycles around
extending the flash life expectancy

## Slide 54: Read Disturb
When reading a bit from NAND flash
there is a small probability that it will flip an adjacent cell
This probability increases with
the number of times the bit is read
the number of PE cycles the block has undergone
To avoid the read disturb errors, the FSP
maintains a counter for each block with the number of reads since the last erase
if the counter exceeds a threshold
  the physical block is copied to a new physical block and the LUT updated
  the block is erased and released to the free block pool

## Slide 55: Program (Write) Disturb
When writing a page to NAND flash
there is a small probability that it deposit some charge on another cell
on selected page but not supposed to be written
or on non-selected page
This charge causes the cell to weakly programmed
but does not damage the cell (it can be completely erased)
The disturbance
can be minimized by sequential writing of pages in the block
can be detected by the write status check
if missed can be managed using ECC

## Slide 56: Garbage Collection (Page Recovery)
Flash is written in pages
but both can only be erased in blocks (e.g., 64 or 128 pages)
A new flash drive, with only erased pages, can be written very rapidly
After extensive use, a flash drive still has available (unused but not yet erased) pages
located alongside pages still in use in a single block
and so can not be rewritten without erasing the whole block
In order to use such pages, the FSP
reads the contents of pages in use
erase the entire block
rewrites the pages still in use to the block
writes the new page of data
This makes writing a new page significantly slower
causing the SDD to slow-down over time

## Slide 57: Writing a New Page on an Old SSD
IN USE 1
IN USE 2
FREE
IN USE 3
FREE
IN USE 4
FREE
FREE
IN USE 5
IN USE 6
FREE
IN USE 7
ERASED
ERASED
ERASED
ERASED
ERASED
ERASED
ERASED
ERASED
ERASED
ERASED
ERASED
ERASED
IN USE 1
IN USE 2
IN USE 3
IN USE 4
IN USE 5
IN USE 6
IN USE 7
ERASED
ERASED
ERASED
ERASED
ERASED
IN USE 1
IN USE 2
IN USE 3
IN USE 4
IN USE 5
IN USE 6
IN USE 7
NEW PAGE
ERASED
ERASED
ERASED
ERASED
IN USE 1
IN USE 2
IN USE 3
IN USE 4
IN USE 5
IN USE 6
IN USE 7
IN USE 1
IN USE 2
IN USE 5
IN USE 4
IN USE 5
IN USE 6
IN USE 7
Notes: free means not in use, but not erased and so not ready to be written

## Slide 58: Write Amplification Avoidance
The perceived slow-down results from write amplification
i.e., more data being written than absolutely necessary
Worst case - updating a single bit could force rewriting a 2MB block
resulting in a write amplification of 16.8 million
Write amplification also results from
wear leveling
idle-time (background) garbage collection
secure erase (restore out-of-box state)
partial page programming (writing less than a full page)
Write amplification has further shortcomings
extra PE cycles reduce the flash lifetime
extra writes consume bus bandwidth and reduce performance
Various algorithms have been developed to minimize write amplification
Notes: background garbage collection - SSDs are constantly moving pages around internally
write amplification of 3, 4, 5 is typical
there are many more mechanisms not mentioned here – too many to cover

## Slide 59: THE END Thanks for your attention
Yaakov (J) Stein