## Slide 1: Communications Security
Yaakov (J) Stein
CTO

## Slide 2: Communications Security
Communications security (COMSEC) means preventing unauthorized access to communications infrastructure and communicated messages, while still providing the communications service between intended parties
Once upon a time this subject was only of interest for military communications
but it is now crucial to businesses and residential customers as well
In the early days of the Internet, the model was trust everyone
In the 1990s the model changed to soft on the inside, hard on the outside
which led to development of access policies, firewalls, etc.
Today the only reasonable policy is
trust no-one
constantly monitor everything
pro-actively search for vulnerabilities

## Slide 3: Threats
Before adopting a security measure, one must understand the threat
Potential threats include :
denial of service (DoS) to all or some parties
theft of service
access to confidential information
modification of information
control of restricted resources
physical damage to resources
Security experts build threat models
what are the risks ?
who are the potential attackers
what at vulnerabilities and attack vectors
before putting countermeasures into effect

## Slide 4: Countermeasures
What can we do to combat threats ?
Physical security – preventing access to communications devices and links
Emission security – preventing interception and jamming
Authorization – preventing unauthorized access to resources
Source authentication – confirming the source of a message
Integrity – preventing tampering with messages
Confidentiality – preventing eavesdropping
DoS blocking – preventing Denial of Service
Topology hiding – thwarting traffic analysis
Anti-hacking – preventing injection of computer malware
Privacy – protecting user’s personal data from mining and directed collection
We are going to deal only with these in this talk!

## Slide 5: Authorization
The first concern is who is given access to resources
AAA (user) Authentication, Authorization, and Accounting
means any mechanism for controlling access to resources
Well-known AAA systems include
TACACS : Terminal Access Controller Access Control System
RADIUS : Remote Authentication Dial-In User Service
DIAMETER : twice as good as RADIUS
Such systems require
a supplicant (party requesting service)
to prove his identity (e.g., via a password)
to an authenticator (which is often hierarchical)
connect to free port
authorized user

## Slide 6: Passwords
A password is a string provided by the supplicant and verified by the server
The server never stores passwords in the open (threat – theft of the password file)
rather stores a crypto-hash (1-way function) of the passwords
Threats to use of passwords:
Guessing of password
Theft of password
Brute-force (exhaustive search) discovery
Countermeasures
Using complex passwords (at least one capital, one numeral, one punctuation)
Using long passwords (thisisareasonablygoodpassword, x!A0 isn’t)
Place delay after wrong guess
CAPTCHAs (Completely Automated Public Turing test to tell Computers and Humans Apart)
Three-factor authentication
  something you are
  something you have
  something you know
password

## Slide 7: Crypto-hashes
In computer science a hash is a function that
maps strings (vectors) of arbitrary length to strings (vectors) of fixed length
ensures that small change in input map to large changes in output
The output length may be much smaller than the input length,
meaning that many inputs map to the same output (collisions!)
A crypto-hash has a further property of being a 1-way function
calculating the hash function is computationally easy
finding an input that produces a given output is computationally hard
You may already know about check-sum and CRC hashes
  these are good for random error correction, but are not crypto-hashes
Well-known crypto-hashes include :
MD5 (no longer considered secure)
Secure Hash Algorithm SHA1 (widely used, no longer considered secure)
Secure Hash Algorithm SHA2 (actually 6 hashes SHA-224,256,384,512,512/224,512/256)
Secure Hash Algorithm SHA3 (new)

## Slide 8: CHAP
How can we use a hash to store passwords ?
when registering the password is crypto-hashed and its hash value stored
the password file/database only contains hash values
from which passwords can not be recovered
upon logging on the password is hashed and the hashes compared
This is great for logging on to a local computer
for communications it would require sending the password in the clear !
How about computing the hash before transmission and transmitting it ?
No improvement, since the eavesdropper would observe the correct hash
and send it (replay attack) !
The solution is a Challenge Handshake Authentication Protocol
authenticator sends a challenge message to the supplicant
supplicant responds with crypto-hash of challenge+password
authenticator compares response with expected hash value
if match supplicant admitted, else rejected

## Slide 9: EAP
Extensible Authentication Protocol is a authentication framework
and runs over links layers (PPP, Ethernet, WiFi)
without needing IP
Originally developed for PPP (extends PPP’s original CHAP)
Dozens of specific methods (EAP-PSK, EAP-MD5, EAP-TLS, EAP-IKEv2, EAP-SIM, EAP-AKA …)
Used as a link layer authentication for WiFi (WPA, WPA2), IEEE 802.1X, …
EAP provides 1-sided authentication (supplicant by authenticator)
it must be run in both directions for mutual authentication
EAP operation
optionally authenticator sends Identity Request to supplicant
optionally supplicant sends Identity response
authenticator sends EAP request with authentication method and data (challenge)
supplicant sends EAP response (or NAK if doesn’t support authentication method)
authenticator sends success or failure

## Slide 10: 802.1X
802.1X is an IEEE standard for authenticating users of a LAN or WLAN
1X defines
3 parties: supplicant, authenticator, and authentication server
an encapsulation of EAP called EAPoL (EAP over LAN)
a Port Access Entity (PAE)
  before authentication only EAPOL traffic can pass through the port
  after authentication all traffic can pass through the port
802.1X was extended in 2010 to authorize security associations and services
in order to support MACsec (802.1AE) and Secure Device Identity (802.1AR)
access network
RADIUS
AAA
server
Authenticator
core network
EAPoL
EAP over RADIUS
supplicant

## Slide 11: Integrity (anti-tampering)
The next attack we need to consider is a Man in the Middle (MiM) attack
Here someone gains access to a NE and can tamper with packets on-the-fly
LSP
compromised
NE
Alice
Bob
Eve

## Slide 12: MACs and HMACs
We can provide integrity using a Message Authentication Code (MAC)
A MAC is a short block of information that
is uniquely determined by the message
verifies that the message has not been modified
i.e., it is highly unlikely that a modified packet has the same MAC (collision)
is difficult/impossible to forge
The MAC is inserted into packet headers
and is verified upon receipt
A Hash-based Message Authentication Code (HMAC)
uses a crypto-hash as a MAC (but block ciphers and other mechanisms can be used)
The simplest way to prevent forging MACs is by using a shared key
Alice calculates MAC from message + key, and inserts into packet
Bob calculates MAC using message + key, and compares to MAC in packet
Eve, not knowing the key, can not forge the MAC

## Slide 13: Source Authentication
Ethernet and IP packets contain Source Addresses (SA)
but these can be readily forged
MACs can also be used to authenticate a packet’s source
that is, to prove that the SA correctly indicates the packet’s source
We can reuse integrity mechanisms (e.g., MACs) to solve this problem !
All that is needed is to have the (H)MAC protect the SA
if the MAC is correct, then the SA indeed belongs to the claimed sender
DA
SA
payload
integrity

## Slide 14: Replay Attacks
Another type of attack is the replay attack
Here the MiM intercepts a packet and resends it multiple times
(transfer$100 → transfer$100, transfer$100, transfer$100, transfer$100)
Integrity and source authentication mechanisms do not detect replay attacks
since the MACs calculate correctly
We can reuse integrity mechanisms (e.g., MACs) to solve this problem !
To defend against replay attacks
add or utilize a packet sequence number field
have the MAC protect the sequence number field
if the same SN is received again, discard packet
DA
SA
payload
integrity
SN

## Slide 15: Confidentiality
An important attack vector is interception
the packet content is observed by unintended parties
The standard countermeasure is encryption
There are two very different types of encryption – symmetric key and public key
Symmetric key encryption is based on the sides having a shared secret
For example, if Alice and Bob have an identical copies of a one-time pad,
i.e., a list of random bits at least as long as the message,
Alice can xor her message with the one-time pad
creating a message unreadable to Eve (who does not have the one-time pad)
Bob can xor the encrypted message with the one-time pad
recovering the original message
Note that if the one-time pad bits are truly random
this is a provably secure system
However, one-time pads need to be very long and are thus hard to use
instead most symmetric encryption algorithms use shared keys

## Slide 16: Symmetric Encryption Using a Shared Key
Simple encryption algorithms are either substitution ciphers
Or permutation ciphers
THIS IS A SECRET MESSAGE
SHARED KEY SHARED KEY SH
LPJJEMSFFTSXKSWYDMPXQAZM
+
=
PLAINTEXT
CIPHERTEXT
S
THIS IS A SECRET MESSAGE
HSITI ESASRTMCE SAEESG
KEYKEY
KEYKEY
KEYKEY
KEYKEY
PLAINTEXT
CIPHERTEXT
P

## Slide 17: DES
Modern symmetric key algorithms use Shannon’s idea
of alternating between S and P stages
In 1977 NIST published the Data Encryption Standard
based on the Feistel algorithm
Inputs
  64 bits of plaintext
  a 56 bit key
Performs 16 rounds of S-boxes and P-boxes
Outputs 64 bits of ciphertext
Due to using a short 56-bit key
since the late 1990s DES is no longer secure against brute-force attacks
(and possibly never was …)
In order to save DES, a method called triple-DES (3DES) was proposed
3DES uses a key of length 3*56=168 bits, but its effective length is 112 bits
NIST allows 3DES use until 2030, but there is something better …

## Slide 18: AES
In 2001 NIST adopted an algorithm called Rijndael
(after its Belgian creators Vincent Rijmen and Joan Daemen)
as the Advanced Encryption Standard
This choice was the result of a 5-year process
in which 15 candidate algorithms were compared
AES
Inputs
  128 bits of plaintext
  a 128/192/256 bit key
Performs 10/12/14 rounds of substitutions and permutations
Outputs 128 bits of ciphertext
AES is approved by the NSA for protection of top secret data (w/ 256 bit key)

## Slide 19: Block Cipher Modes (1)
The encryption mechanisms we have discussed so far are block ciphers
that is, they operate on blocks of N bits
But how do we use a block cipher to encrypt an arbitrary sized message ?
The simplest method is Electronic codebook (ECB)
which performs the block cipher independently on each N bits
(if needed, the last block is padded with zeros)
If the input repeats itself, ECB encrypts in the same way
revealing patterns in the plaintext (leakage - aiding the cipher breaker)
ECB is also susceptible to replay attacks
Thus, ECB should never be used
What can be done ?
Instead of encrypting the plaintext,
we can xor the plaintext with the previously encrypt block before encrypting
encrypt the previous ciphertext and then xor with the plaintext
or even encrypt something else entirely (e.g., a counter) and xor with the plaintext

## Slide 20: Example of ECB’s failure
original
AES-ECB
AES-CBC
All patches of the same color in the original picture
are encrypted by ECB to the same value
This results in significant leakage
which can be exploited to recognize the picture and recover the secret key
CBC does not exhibit this negative characteristic
pictures by Phillip Wang

## Slide 21: Block Cipher Modes (2)
Cipher block chaining CBC
Counter mode CTR
Galois Counter Mode GCM is CTR using Galois field operations

## Slide 22: Block Cipher Modes (3)
Cipher feedback CFB
Output feedback OFB

## Slide 23: Key Exchange / Distribution
The problem with symmetric key encryption
is that both parties must possess the shared key
This requires:
face-face meetings
trusted couriers
synchronized key generators
using an existing (but perhaps compromised) secure channel
This makes symmetric encryption logistics a nightmare
For many years mathematicians searched for a solution to this problem
it was first solved in principle in GCHQ by James Ellis (idea) and Chris Cocks (1-way function) but remained unknown to the public as it was classified
key exchange was solved by Martin Hellman
public key was solved in theory by Whitfield Diffie (idea) and Ron Rivest (1-way function)

## Slide 24: My classification
We can explain 4 types of encryption by the following analogies
Shared-key (symmetric) encryption (e.g., DES, AES)
Alice and Bob both have identical copies of a the key to a strong-box
Alice puts her message in the box, locks it with her key, and sends to Bob
Bob uses his identical key to open the box and recovers the message
One private key encryption (e.g., RSA or ECC)
Bob has the key to open a box that locks automatically upon closing (1-way function)
Bob sends open box to Alice, Alice puts message in box, closes, sends back to Bob
Bob opens the box with his key
Two private key encryption (e.g., RSA or ECC with signature)
Alice has a locking key and Bob has an unlocking key to a strong-box
Alice puts her message in the box, locks it with her locking key, and sends to Bob
Bob unlocks the box with his unlocking key, and recovers Alice’s message
Multi-exchange (e.g., DH)
Alice puts her message in the box, locks with her padlock, and sends to Bob
Bob places his padlock alongside Alice’s, locks, and sends back to Alice
Alice removes her padlock, and sends back to Bob
Bob removes his padlock, and recovers the message

## Slide 25: First attempts to encrypt without keys
Can we use one-time pads to communicate without shared secrets ?
ATTEMPT 1 – substitution code
Alice xors message M with a one-time pad A and sends D1 = M + A to Bob
Bob xors D1 with his one-time pad B and sends D2 = M + A + B to Alice
Alice xors D2 with her old one-time pad A and sends D3 = M + A + B + A = M + B
Bob xors D3 with his old one-time pad B and recovers D3 + B = M + B + B = M
While the data of each transmission Dn is safe
if Eve observes all the transmissions, she can recover the message
Eve observes D1 = M + A, D2 = M + A + B, and D3 = M + B
Eve xors D1 + D2 + D3 = B + D3 = M BROKEN
ATTEMPT 2 – permutation code
Alice permutes M with a one-time permutation A and sends D1 = A*M to Bob
Bob permutes D1 with his one-time permutation B and sends D2 = B*A*M B to Alice
but permutations don’t commute!
so if Alice permutes D2 with the inverse of her old one-time permutation
she obtains D3 = A-1 * B * A * M ≠ B*M DOESN’T WORK

## Slide 26: Public key cryptography
Two things are missing to make this idea work:
one-way functions
greater mathematical sophistication
The breakthrough is public key cryptography (AKA asymmetric cryptography)
With this method each party has a public key and a private key
Public keys may be advertised
but private keys are kept private
Operation
Alice encrypts the message using Bob’s public key (and optionally her private key*)
Bob decrypts it using his private key (and optionally Alice’s public key)
Eve, not knowing the private key, can not decrypt the message
So no key distribution is needed
although you still have to ensure that Alice’s public key is authentic
* if authentication is desired

## Slide 27: Digital Signatures
Another application of public key cryptography is digital signatures
If a message is digitally signed by Alice
then Bob can verify that Alice really signed it, and not Eve
The idea behind the use of public key methods is
the signature proves that the signer had access to the private key
the private key is not divulged
Operation
Alice signs the message with her private key and sends to Bob
Bob can verify the signature using Alice’s public key
as a side effect, the verification also ensures integrity
Note that this is a kind of source authentication
but different from a MAC
since a MAC relies on a shared secret

## Slide 28: Public key algorithms
Public-key cryptography (asymmetric cryptography)
relies on mathematical calculations that are hard to perform, such as
factoring large integers
it is easy to multiple 2 large primes p and q to find n = pq
but it is hard to factor n to find p and q
finding discrete logarithms (and related : computational DH, decisional DH)
given a finite group G
it is easy to multiply an element b with itself n times to find g = bn
but it is hard to find given b and g to find n such that bn = g
elliptic curve logarithms
given an elliptical curve y2 = x3 + ax + b over the field Fp
(elements 0 … p-1 with all operations modulo p)
it is easy to perform the EC multiplication operation
of element b with itself n times to obtain bn = b . b . b … = g
but it is hard given b and g to find n such that bn = g
WARNING – with quantum computers the complexity is reduced

## Slide 29: RSA
RSA was one of the first public key algorithms to be discovered
Named after Ron Rivest, Adi Shamir, Leonard Adleman who published it in 1977 although discovered earlier in GCHQ but classified
RSA is based on the facts that
it is easy to multiple 2 large prime numbers
it is hard to factor the product to recover the prime numbers
It is an open problem in mathematics whether factoring is indeed hard
To use:
find two large prime numbers and multiply them
based on number theory create public and private keys
sign messages using private key or
encrypt messages using recipient’s public key
RSA was patented (by RSA Security Inc., founded by R, S, and A) but expired in 2000
there are rumors that RSA placed backdoors in their products for the NSA
RSA Security was acquired by EMC in 2006, which was acquired by Dell in 2016
RSA is still often used instead of stronger elliptical curve methods
due to the latter having patents in force

## Slide 30: RSA algorithm
Preparation
Bob selects two large primes p and q (there are many methods to find primes)
Bob calculates n = pq and Φ=(p-1)(q-1)
Bob selects e between 2 and Φ-1 which is co-prime to Φ
Bob computes d such that ed = 1 mod Φ (using Euclid’s algorithm)
Bob publishes {n, e} as his public key, and keeps d as his private key
Mathematical background
Raising M to the e power modulo n : Me mod n
  is a 1:1 transform
  is a one-way function
if C = Me mod n then M = Cd mod n (follows from Fermat’s little theorem and CRT)
Operation
Alice encrypts her message M into ciphertext thus: C = Me mod n
and sends to Bob
Bob decrypts thus : Cd mod n = M
Eve, not knowing p and q and thus not d, can not recover M

## Slide 31: El Gamal
Discrete logarithm cryptosystem published by Taher Elgamal in 1985
PhD under Hellman, chief scientist at Netscape where he was father of SSL
director engineering and afterwards CEO of RSA Security Inc., now CTO for security at SalesForce
and used in NIST’s Digital Signature Standard
Preparation
Bob chooses a cyclic group G of order q with generator g
Bob chooses a random number x between 1 and q-1
Bob computes h = gx
Bob publishes {G, q, g, h} as his public key, and keeps x as his private key
Operation
Alice randomly chooses an ephemeral key y between 1 and q-1
Alice calculates c1 = gy
Alice calculates the shared secret s = hy
Alice encodes her message as an element m of G and calculates c2 = ms
Alice sends the ciphertext (c1 ,c2) to Bob
Bob calculates the shared secret s = c1x = gyx = gxy = hy
Bob calculates the inverse of s : s-1= c1q-x = g(q-x)y
Bob recovers the message m = c2s-1 = ms s-1
Eve, not knowing x, can not find s or s-1

## Slide 32: Certificates
I can be sure of Alice’s public key if she personally hands it to me
if I am just given it – it may be forged by Eve !
How can we be sure of someone else’s public key ?
The idea is to have someone trusted (i.e., for whom we already have a public key) vouch for it
How can that trusted party be sure ? Someone he trusts vouches for it!
There are two methods to implement this
Public Key Infrastructure (e.g., X.509)
web of trust (e.g., PGP)
X.509 is an ITU-T standard for PKI
It specifies the format of certificates
and a strict hierarchical system of Certificate Authorities that can issue them
With the web of trust model anyone (not just special CAs) may sign certificates

## Slide 33: Secure key exchange
Using public key cryptography no key distribution is required
However, public key encryption is computationally much more expensive
than symmetric encryption
One solution to this problem is to re-use public key cryptography
We only use public key encryption to encrypt a (symmetric) key
all the messages are sent using inexpensive symmetric cryptography
Operation
Alice encrypts a random key using her private key and Bob’s public key
Bob decrypts the key using his private key and Alice’s public key
Alice and Bob now communicate using symmetric encryption
after some amount of key use, the process is repeated

## Slide 34: Diffie–Hellman key exchange
We do not need full public key cryptography to distribute symmetric keys
The original DH was published by Whitfield Diffie and Martin Hellman in 1976
although discovered earlier in GCHQ but classified
DH is based on the field Fp (numbers 0 … p-1, with operations modulo p)
Operation
Alice and Bob agree to use a prime number p and a primitive root g
(g is a primitive root, if every number is congruent to gn for some n)
Alice chooses a secret integer a and sends to Bob A = ga mod p
Bob chooses a secret integer b and sends to Alice B = gb mod p
Alice now computes s = Ba mod p = gba mod p
Bob now computes Ab mod p = gab mod p = s
Alice and Bob now share the secret s
Alice and Bob now use s as a symmetric key !
Eve, not knowing a or b, can not deduce s

## Slide 35: Diffie Hellman Groups (RFC 7296)
0 | NONE |  | [RFC7296]
1 | 768-bit MODP Group | [RFC6989], Sec. 2.1 | [RFC7296]
2 | 1024-bit MODP Group | [RFC6989], Sec. 2.1 | [RFC7296]
3-4 | Reserved |  | [RFC7296]
5 | 1536-bit MODP Group | [RFC6989], Sec. 2.1 | [RFC3526]
6-13 | Unassigned |  | [RFC7296]
14 | 2048-bit MODP Group | [RFC6989], Sec. 2.1 | [RFC3526]
15 | 3072-bit MODP Group | [RFC6989], Sec. 2.1 | [RFC3526]
16 | 4096-bit MODP Group | [RFC6989], Sec. 2.1 | [RFC3526]
17 | 6144-bit MODP Group | [RFC6989], Sec. 2.1 | [RFC3526]
18 | 8192-bit MODP Group | [RFC6989], Sec. 2.1 | [RFC3526]
19 | 256-bit random ECP group | [RFC6989], Sec. 2.3 | [RFC5903]
20 | 384-bit random ECP group | [RFC6989], Sec. 2.3 | [RFC5903]
21 | 521-bit random ECP group | [RFC6989], Sec. 2.3 | [RFC5903]
22 | 1024-bit MODP Group with 160-bit Prime Order Subgroup | [RFC6989], Sec. 2.2 | [RFC5114]
23 | 2048-bit MODP Group with 224-bit Prime Order Subgroup | [RFC6989], Sec. 2.2 | [RFC5114]
24 | 2048-bit MODP Group with 256-bit Prime Order Subgroup | [RFC6989], Sec. 2.2 | [RFC5114]
25 | 192-bit Random ECP Group | [RFC6989], Sec. 2.3 | [RFC5114]
26 | 224-bit Random ECP Group | [RFC6989], Sec. 2.3 | [RFC5114]
27 | brainpoolP224r1 | [RFC6989], Sec. 2.3 | [RFC6954]
28 | brainpoolP256r1 | [RFC6989], Sec. 2.3 | [RFC6954]
29 | brainpoolP384r1 | [RFC6989], Sec. 2.3 | [RFC6954]
30 | brainpoolP512r1 | [RFC6989], Sec. 2.3 | [RFC6954]
31 | Curve25519 | [RFC8031], Sec. 3.2 | [RFC8031]
32 | Curve448 | [RFC8031], Sec. 3.2 | [RFC8031]
MODP = MODular Prime
ECP = Elliptical Curve mod Prime
brainpool – see RFC 6954

## Slide 36: Where to apply security ?
Every layer of the user plane can benefit from security mechanisms
Control and management planes have their own mechanisms
PHYSICAL
LINK
NETWORK
TRANSPORT
SESSION
PRESENTATION
APPLICATION
PHYSICAL
LINK
NETWORK
TRANSPORT
SESSION
PRESENTATION
APPLICATION
physical site security
PHY encryption
802.1X, MACsec
IPsec
HTTPS, SSH, SFTP, …
TLS, SSL
TCP authentication option

## Slide 37: IPsec
IP was designed when security was not an issue
IPsec is a set of open standards that rectify many of IP’s deficiencies
IPsec is transparent to applications (apps needn’t know that it will be used)
IPsec is based on the concept of a security association (SA)
SA is a relationship between two or more entities
describes how the entities will securely communicate
specifies which security features (authentication, integrity, encryption) will be used
specifies algorithms (DES, AES, SHA-1, RSA, …) and options
takes care of key exchange (ISAKMP Internet Security Association and Key Management Protocol )
  pre-shared keys
  Internet Key Exchange (IKE, IKEv2)
  IPSECKEY DNS records
Internet Key Exchange (UDP port 500) is used for establishing IPsec sessions
(performing mutual authentication, establishing and maintaining SAs, key exchange)

## Slide 38: IPsec modes
IPsec has two different modes of operation
Transport Mode
  IPsec header is inserted into an existing packet (between IP and TCP headers)
packet routing is unaffected, but NAT traversal may be (new protocol numbers)
adds security functionalities to existing flow
if encrypting, TCP (or UDP) header is encrypted
Tunnel Mode
entire IP packet is encapsulated (and optionally encrypted)
can be used to create IPsec VPN
IP
TCP
PAYLOAD
IP
TCP
PAYLOAD
IPsec
IP
TCP
PAYLOAD
IPsec
IP’
transport mode
tunnel mode

## Slide 39: AH and ESP
IPsec has two different formats
Authentication Header (AH)
supports source authentication and data integrity only
protection
  in transport mode protects payload and header fields except mutable
  (e.g., TTL, DSCP, header checksum, offset, flags)
  in tunnel mode protects entire packet
uses protocol number 51
Encapsulating Security Payload (ESP)
supports source authentication, data integrity, and encryption
  similar to AH if null encryption is used
adds trailer(s) in addition to IPsec header
protection
  in transport mode doesn’t protect IP header (but does TCP header)
  in tunnel mode entire packet is protected
uses IP protocol 50

## Slide 40: IPsec packet formats
IP
TCP
PAYLOAD
AH
IP
TCP
PAYLOAD
AH
IP’
AH transport mode
AH tunnel mode
Authenticated (except mutable)
Authenticated (except mutable)
IP
TCP
PAYLOAD
ESP trailer
ESP transport mode
ESP tunnel mode
Authenticated
ESP auth
ESP header
Encrypted
IP’
TCP
PAYLOAD
ESP trailer
Authenticated
ESP auth
ESP header
Encrypted
IP
Note: AH and ESP headers contain “next header” fields
for tunnel mode these are set to 4 (IPv4) or 41 (IPv6)
for transport mode these are set to 6 (TCP) or 17 (UDP)

## Slide 41: IPsec algorithms
RFC 4835 was the specification of supported algorithms for IPsec
Authentication
MUST HMAC-SHA1-96
SHOULD+ AES-XCBC-MAC-96
MAY HMAC-MD5-96
Encryption
MUST NULL
MUST AES-CBC with 128-bit keys
MUST- 3DES-CBC
SHOULD AES-CTR
SHOULD NOT DES-CBC
MAY AES-CCM and AES-GCM

## Slide 42: IPsec algorithms
RFC 7321 is the most recent specification of supported algorithms for IPsec
Combined
SHOULD+ AES- GCM with 128 bit key (MAY 192 or 256)
MAY AES-CCM with 128 bit key (MAY 192 or 256)
Authentication
MUST HMAC-SHA1-96
SHOULD+ AES-GMAC with AES-128
SHOULD AES-XCBC-MAC-96
MAY NULL (for ESP only)
Encryption
MUST NULL
MUST AES-CBC with 128-bit keys (MAY 192 or 256)
MAY AES-CTR with 128-bit keys (MAY 192 or 256)
MAY 3DES-CBC
MUST NOT DES

## Slide 43: Suite B
RFC 6379 and 6380 detail an alternative suite of IPsec algorithms
This suite mandates AES-GCM with 128 or 256 bit keys
Suite-B-GCM-128
  IPsec with AES-GCM-128 including encryption
  IKE with AES-CBC-128, HMAC-SHA-256 and DH group 19 (256 bit ECP)
Suite-B-GCM-256
  IPsec with AES-GCM-256 including encryption
  IKE with AES-CBC-256, HMAC-SHA-384 and DH group 20 (384 bit ECP)
Suite-B-GMAC-128
  IPsec with AES-GCM-128 without encryption
  IKE with AES-CBC-128, HMAC-SHA-256 and DH group 19 (256 bit ECP)
Suite-B-GMAC-256
  IPsec with AES-GCM-256 without encryption
  IKE with AES-CBC-256, HMAC-SHA-384 and DH group 20 (384 bit ECP)

## Slide 44: MACsec
802.1AE MACsec was approved in June 2006
based on well known AES-128 encryption
  but with a new mode - Galois Counter Mode
  AES/GCM uses a single algorithm for integrity and encryption
MACsec
works over Connectionless network by forming secure associations
integrated into Ethernet frame format
provides
  source authentication
  confidentiality
  connectionless data integrity
  replay protection
  limited blocking of DoS attacks
may degrade some QoS attributes (e.g. introduces bounded delay)

## Slide 45: MACsec format
SecTAG contains
MACsec Ethertype (88E5)
4B Packet Number (sequence number)
8B Secure Channel Identifier
ICV is a 16B Integrity Check Value
12 B Initialization Vector
DA
SA
Type
payload
FCS
DA
SA
secure data
FCS’
SecTAG (incl. IV)
ICV
integrity
optional
confidentiality

## Slide 46: TLS (and SSL)
Sometimes it is better to provide security at a layer higher than L3
For these cases there is Transport Layer Security (and previously versions of SSL)
Heartbleed bug in OpenSSL scared the whole world in April 2014
TLS
adds integrity and encryption to client/server applications
  https, smtp/pop/imap, sips, mysql, EAP-TLS…
is based on SSL (developed by Netscape)
is widely used to secure web browsing (https), email, ecommerce, etc.
client picks a random number, encrypts with server's public key and sends to server
client and server can now communicate using symmetric encryption and MACs
Compared to IPsec, TLS
can be implemented in a browser (e.g., for online banking or commerce)
and doesn’t require/trust OS kernel support like IPsec VPNs
only runs over connection oriented TCP (but there is DTLS is for UDP)
can authenticate individual users, rather than IP source addresses
is better than IPsec at NAT traversal

## Slide 47
Yaakov (J) Stein
CTO