## Slide 1: המאגד לניטור תעבורה מוצפנת
יום הדגמה & יום עיון אקדמיה
Trends in
Encrypted Traffic
Y(J)S

## Slide 2: Isn’t almost all traffic encrypted already?
It is frequently said that >85% of Internet traffic is encrypted
What this really means is that 85% of the Internet Traffic volume
is https, i.e., http / TLS / TCP / IP
with TLS 1.3 providing more than adequate security
DPI engines thrive in this scenario, correctly inferring
application type
specific application
specific modes or events
device type
QoE
about 95% of the time

## Slide 3: Information leakage - SNI
This is because DPI engines exploit information leakage
mostly from packet fields that are still unencrypted
A notable (but far from the only) example is SNI
The TLS handshake, in which the sides agree on encryption mechanisms
consists of a Client Hello message followed by a Server Hello
The CH specifies
the cyber suites the client supports
various crypto-related parameters
optionally the name of the server (SNI) the client wants to reach
since there may be many virtual servers hosted behind a single IP address!
Since the cyber suite has not yet been agreed upon
the CH message is unencrypted, and thus leaks SNI and other information

## Slide 4: Information leakage - unencrypted DNS
Another notable source of information leakage is unencrypted DNS
Domain Name System allows a client to find the IP address of a service (domain name)
A DNS exchange consists of a request and a response
the client request asks a DNS resolver to provide information
e.g., given a domain name what are the IP addresses
the resolver’s response provides the answer
e.g., domain name corresponds to the following IP addresses
By observing a DNS response message
we learn both what domain the client is interested in,
and the mapping of a server IP address to that domain
When packets are seen from the client to an IP addressed specified in the DNS response
we know the service being consumed

## Slide 5: Information leakage - misc.
SNI and DNS responses are only 2 sources of information leakage
there are many other information leakages that can help in our task
other TLS fields (ALPN, options, TLS fingerprinting)
UDP/TCP port numbers
TCP flags and options
server IP address
other IP fields (TTL, DSCP)
packet sizes
traffic volumes

## Slide 6: So, what has changed?
Over the past few years Internet traffic is becoming more fully encrypted
Fully encrypted traffic minimizes leakage
in order to increase the privacy of the IP protocol suite
In particular
Encrypted DNS (DoT, DoH, DoQ), as its name implies,
  encrypts DNS responses
  hiding the domain-IP address mappings
Encrypted Client Hello, as its name implies,
encrypts the TLS CH message
using a public key obtained, e.g., from a new DNS response message
hiding the SNI and other TLS CH fields

## Slide 7: Why has this happened?
About a decade ago Edward Snowden disclosed
mass surveillance of US domestic telecommunications by the NSA
NSA received information from
OTTs such as Google, Facebook and Amazon
CSPs such as Verizon and AT&T
Many people were not overly disturbed by the revelations
being accustomed to trading off privacy for services/convenience
But many communications/networking experts were outraged
at the undermining of their protocols
and were determined to enhance the privacy of the IP protocol suite

## Slide 8: Privacy vs. Security
Cyber security and privacy often overlap, but are fundamentally distinct
Security is protection against threats, e.g.,
  unauthorized data access
  malicious data modification or erasure
  denial of service
  physical damage to resources
Privacy is the right to control personal information, e.g.,
  hinder impersonation and identity theft
  thwart theft based on knowing identity-related data
  block tracking of an individual’s behavior

## Slide 9: Does hiding information only from CSPs make any sense?
The focus of privacy enhancing mechanisms has been on hiding
privacy-invasive information from service providers / network operators
but little has been done about the OTTs
whose entire business model is based on monetizing personal data
In fact, the NSA received most of its privacy-sensitive data from OTTs !
But
people are willing to trade some personal information for free service
CSPs use standards developed by privacy-conscious SDOs
while OTTs use proprietary software with little public visibility
OTTs spend tremendous sums on lobbying

## Slide 10: The downsides of privacy
Sometimes privacy and security can actually be antagonistic
rather than complementing one another
For example, privacy-enhancement may hide information
that enables malware blocking and botnet detection
And privacy-enhancing encryption can also make legitimate SP tasks, e.g.,
  traffic management
  differentiated charging
  DDoS blocking
  geolocation-based services and IPR restrictions
  fault isolation, network planning
  much more difficult, or even impossible

## Slide 11: Less information leakage - DNS and TLS
DoT DNS over TLS
first draft October 2014
RFC 7858 May 2016
DoH DNS over HTTPS
first draft May 2017
RFC 8484 October 2018
public DNS support late 2019
Chrome default since May 2020
DoQ DNS over QUIC
first draft April 2017
RFC 9250 May 2022
TLS 1.3
first draft April 2014
RFC 8446 August 2018
eSNI
first draft July 2018
extended to ECH March 2020
ECH
WG LC March 2024
expect RFC Q1 2025
early adopters H4 2024
broader adoption 2025

## Slide 12: Less information leakage - QUIC
QUIC is a new TCP-like L4 protocol that was invented to speed up http
and it was not invented for privacy/security reasons
However, being a modern design, it contains many novel features
almost everything in almost all packets is encrypted
handshake packets are obfuscated, with SALT changing between versions
data put into frames that are muxed together
multiple streams can be muxed in a single flow (enabling MASQUE VPNs)
connection identifiers can unexpectedly migrate
GREASE Generate Random Extensions And Sustain Extensibility is liberally applied
unencrypted bits meaning is changed between versions
random delays added to confuse monitoring

## Slide 13: Even less information leakage - PQC
All leakage blockage mechanisms are based on public-key cryptography
Public-key crypto depends on one-way functions
mathematical problem that are easy to compute but hard to reverse
such as factoring large semi-primes or finding discrete logarithms
It turns out that although these problems
are exponentially (?) hard for a conventional computer
they are polynomially easy for a Cryptographically Relevant Quantum Computer
No CRQC currently exists, but there may be in 5-10 years (or 50 years, or never)
To protect against Harvest Now Decrypt Later strategies
Post Quantum Cryptography methods have been devised
and NIST has standardized 4 such algorithms (including ML-KEM = Kyber)

## Slide 14: PQC recent adoption timeline
Common practice is to adopt a hybrid Key Exchange Method
since PQC methods have not been sufficiently studied
and we aren’t sure enough that there are no classical attacks
Chrome now defaults to offering X25519Kyber768
Firefox now supports Kyber
Apple has announced a different hybrid KEM for iMessage
ExpressVPN’s Lightway now defaults to hybrid TCP:P512Kyber768 UDP:P256Kyber512
Signal now uses ECC(x25519 or c448)+SHA2(256 or 512)+Kyber1024
Tuta is using X25519Kyber1024 for email and file storage

## Slide 15: Exceptionally less information leakage - Oblivious X
Even if we encrypt all fields in TCP, TLS, and above
forwarding requires that we leave the IP addresses and we can still use IP reputation
However, there are methods that use proxies to hide IP addresses
OHTTP (RFC 9458)
Apple Private Relay (iCloud Private Relay) adopted MASQUE (based on QUIC)
Whatsapp Protect your IP address metadata
Google’s IP protection (ex-GnatCatcher)
client IP visible
but not server IP
server IP visible
but not client IP
neither IP visible

## Slide 16: Ridiculously low leakage - metadata obfuscation
Even if we can’t see even IP addresses
we can see PPI - packet times, sizes and directions
Proposed traffic obfuscation mechanisms (PriFi, Loopix, BuFLO, TARANET ditto)
divide/merge/pad all packets to same length
(sophisticated methods reduce added overhead to < 10%)
add chaff packets
delay packets to disguise interpacket timing behavior
So, basically all that is left is the session duration
which can be further disguised by connection migration

## Slide 17: Timeline of a few of the DPI challenges
2023
2025
2024
Chrome enables DoH by default
Chrome enables ECH + GREASE
Cloudflare turns on ECH first time
Cloudflare turns off ECH
Cloudflare turns ECH back on for free accounts
Google to offer IP Protection (?)
Apple turns on APR for Safari browser only
Chrome enabled Kyber+X25519 by default
Apple to turn on APR for all iPhone/MAC connections (?)
NIST CNSA 2.0 (PQ key exchange + authentication) initial deployments
Cloudflare turns on ECH for free accounts
DoQ RFC
Facebook ECH experimentation
Cloudflare to turn on ECH for all accounts
ECH ramp-up phase
ECH RFC
Chrome starts using baked-in public DNS resolvers
QUIC ramp-up
earlier
DoH RFC
near universal adoption of https

## Slide 18: What’s holding up ECH?
ECH was proposed way back in 2018
and all major browsers now support it
why aren’t servers supporting it yet?
chicken and egg problem (similar to what happened to IPv6)
without encrypted DNS there is little reason to use ECH
and without ECH there is little reason to use encrypted DNS
most DNS traffic is towards network infrastructure DNS
and many operators don’t want encrypted DNS
ECH is a complex extension - several subtle bugs have caused problems
e.g., Cloudflare disabled after a short period
the main way to distribute the initial key (every hour or two) is via DNS
and the operational aspects of updating keys are not fully worked out

## Slide 19: A more realistic server ECH timeline
Cloudflare now forces free customers to use ECH
and from Q1/2025 will default to using for all customers
but allow disabling form the dashboard
Major players (other than Cloudflare) are not on-board
Google servers have no plans, FB has only an experimentation roadmap
The RFC is mysteriously held up once again
and most (other than Cloudflare and testing sites) will use before RFC
A realistic timeline is for low percentage of sites to start rolling out in 2025
a more significant fraction in 2026
and a long tail of non-ECH sites for > 5 years